| BenQ Projector RS232 code for SP830/SP831 |
| --- |
| Code | Function | Comment |
| 0x06 0x14 0x00 0x03 0x00 0x34 0x11 0x00 0x5c | power on | It should be send by hex format |
| X001X | Power off | System operation |
| X003X | Menu | OSD operation |
| X004X | Enter | OSD operation |
| X005X | Exit | OSD operation |
| X006X | Up | OSD operation |
| X007X | Down | OSD operation |
| X008X | Left | OSD operation |
| X009X | Right | OSD operation |
| X041X | Load preset 'cinema' mode | Load settings |
| X042X | Load preset 'home theater' mode | Load settings |
| X043X | Load preset 'family room' mode | Load settings |
| X044X | Load preset 'photo' mode | Load settings |
| X045X | Load preset 'gaming' mode | Load settings |
| X046X | Load from user's memory 1 | Load settings |
| X047X | Load from user's memory 2 | Load settings |
| X048X | Load from user's memory 3 | Load settings |
| X049X | Load default of all user OSD | Load settings |
| X091X | Lamp ECO Mode (200W) |  |
| X092X | Lamp Normal Mode (250W) |  |
| X093X | Disable Auto Source Searching |  |
| X112X | Color Temp: LampNative |  |
| X113X | Color Temp: Warm |  |
| X114X | Color Temp: Normal |  |
| X115X | Color Temp: Cool |  |
| X116X | Color Temp: User1 |  |
| X117X | Color Temp: User2 |  |
| X118X | Color Temp: User3 |  |
| X131X | CVBS | Input source select |
| X132X | S-Video | Input source select |
| X133X | RGB-HD | Input source select |
| X134X | HDMI | Input source select |
| X135X | YPbPr 1 | Input source select |
| X136X | YPbPr 2 | Input source select |
| X137X | YCbCr 1 | Input source select |
| X138X | YCbCr 2 | Input source select |