Question:  Do you have a telephone interface for the ProAnnounce System so that paging can be done from a customer's existing phone system?  If so, what can you do with it?

Answer:  YES!  We have the DTI2000 Digital Telephone Interface.

The DTI2000 is programmed EXACTLY the same way as our Digital Paging Consoles.  Therefore, anything you can do with a paging console (paging individual zones, groups of zones, all call, turning on strobes, lights, water fountains, motors, setting off messages etc...) can be done with the DTI2000 through a telephone system.  Dialing into a DTI2000 is simple and can be done with a hard-wired phone, wireless phone or even a cell phone!

The DTI2000 will do some incredible things when combined with a ProAnnounce System.  Here are some of it's features: 
* 100 zones available 
* Up to 20 calling groups 
* Selection of single zones, multiple zones or groups for announcements 
* Prerecorded message triggering (message playback) 
* Special function triggering (macros) 
* Programmable priority for announcements and messages 
* Two-level password protection 
* Acknowledgement signals 
* Automatic hang-up 
* Front panel audio level control 
* One rack space height 

The DTI2000 is a microprocessor-controlled, configurable telephone interface that allows a ProAnnounce System to be connected to a telephone installation or the phone network.  The half rack width DTI2000 provides the user with a full functioning paging interface over a standard analog phone line.  Even digital telephone systems must provide an analog phone line connection allowing you to use a DTI2000 on these types of systems.  You DO NOT need a paging console to connect the DTI2000 to the DPM4000 Matrix Manager.  Simply plug the DTI2000 into a paging console input module on the DPM4000.  Remote triggering of signals, prerecorded messages, pre-chime signals and control functions (macros) within the ProAnnounce system are all possible via the DTI2000. 

The DTI2000 uses DTMF tones and connects to a standard analog plain old telephone system (POTS) telephone line.  There are also audio beeps to interact with the user for OK, busy, text message in progress etc...  Two levels of password protection are provided to prevent unauthorized access to system functions.  Audio from the caller is metered and adjusted with a level control from the front panel. 



The DTI2000 includes RS-485 and RJ-12 connectors (cable included) for programming and interface with the DPM4000.  It also includes two (2) RJ-11 telephone jack sockets (loop thru) for connection to the analog phone line and/or another DTI2000 (yes, you can "gang" them and program each of them with identical routines for simultaneous paging to two different zones and have either one take priority over the other one for emergency paging, especially useful in Hospitals for "code blue" pages).  There is even a "side-by-side" rack mount for two units.