1

| ES-2000 Amplifier/ | Receiver |
| --- | --- |
| Number of Channels | 2 |
| Frequencies | Ch. 1: 2.3 MHz Ch. 2: 2.8 MHz |
| Maximum Deviation | 40 KHz |
| Signal to Noise | >80 dB (SINAD @ 40 KHz dev / 1KHz tone) |
| THD | <1% (28 KHz dev / 1 KHz tone) |
| Acoustic Output | 4 Channels x 13 W rms, 52 W rms total |
| Speaker Load | 8 Ohms |
| Power Supply | 120 VAC- Inboard Power Supply |
| Dimensions | 17” x 12” x 1.75” (1 rack width length x 1 rack width high) |
| Weight | 12 lbs |
| ES-BT2, Body Pack | Transmitter |
| Number of Channels | 2 (switch Ch. 1/Ch. 2) |
| Frequencies | Ch. 1: 2.3 MHz Ch. 2: 2.8 MHz |
| Size | 3.9” x 2.7” x 1.0” |
| Weight | 5.1 oz (with battery) |
| Battery Type | 2 AA Batteries (two NiMH AA Included) |
| Battery Drain | 160 mA drain |
| Battery Capacity | 2000 mAh |
| ES-HT2 Hand Held | Transmitter (Optional Accessory) |
| Number of Channels | 2 (switch Ch. 1/Ch. 2) |
| Frequencies | Ch. 1: 2.3 MHz Ch. 2: 2.8 MHz |
| Microphone Type | Uni-Directional, Dynamic |
| Size | 2.28” x 10.04” |
| Battery Drain | 100 mA drain |
| Speaker: Ceiling Dome | (Speaker Option One) |
| Speaker Type | Ceiling Dome, six, 4-inch speakers |
| Impedance | 8 Ohms |
| Capacity | 50 Watts |
| Sensitivity | 87 dB |
| Frequency Response | 150 to 11,000 Hz |
| Size | 24” x 24” x 8” (fits in a 2 x 2 ceiling tile space) |
| Weight | 14 lbs |
| Speaker: Bookshelf | Two, ClassMate 4.2 Speakers (Speaker Option Two) |
| Speaker Type | ClassMate 4.2, two, 4-inch woofers & one, 1-inch titanium tweeter, each (speakers by Electro-Voice) |
| Impedance | 8 Ohms |
| Capacity | 200 Watts |
| Sensitivity | 89 dB |
| Frequency Response | 65 to 20,000 Hz |
| Size | 12.2” x 6.9” x 8.5” |
| Weight | 8.5 lbs (each) |
| Speaker: Ceiling Cans | Four, ClassMate C4.2 Speakers (Speaker Option Three) |
| Speaker Type | ClassMate C4.2, one, 4-inch woofer & one, 1-inch titanium tweeter, each (speakers by Electro-Voice) |
| Impedance | 8 Ohms |
| Capacity | 80 Watts |
| Sensitivity | 86 dB |
| Frequency Response | 65 to 20,000 Hz |
| Size | 6.9” x 7.1” |
| Weight | 6.0 lbs. (each) |
| External Infrared Sensor | (2 Included per system) |
| Power | Powered by Receiver/Amplifier |
| Number of Diodes | 3 Jumbo Diodes, each |
| Size | 2” x 3” x 1” |
| Weight | 4 oz. |
| Type of Cable | Coaxial Cable (RG-59) |
| Number of Cables | 2 |
| Cable Sizes | Cable 1: 12 Inches Cable 2: 50 Feet |

Last Updated: 12/02/03

# Text boxes

ESIR-2000

ESIR-2000