JBL Power Ratings Compared to EV

For bass speakers JBL used the AES method:

50-500 Hz band limited “pink” noise (or shaped noise) for 5 min

For full range speakers, JBL used the IEC rating:

50-5kHz shaped noise for 2 hours

This is a simple test that makes their speakers look better than ours that are tested with more vigor:

EIA Loudspeaker Power Rating Full Range (EIA RS-426-A 1980) uses a noise spectrum, which mimics typical music and tests the thermal and mechanical capabilities of the components. This is an eight-hour test.  6dB peaks are also inserted.