A Few Tips

- Put associated microphone and speaker zones on the same unit.

- Putt all items that need to be in an EC ref on the same unit.

- Put the base configuration in a preset so that it is easy to get back to the starting point.

- Develop standards for macros and presets

- Do not route far-end audio via a routing switcher.

- Use the print function to document the setup

- Use copy/paste to speed up site fine set-up.

- Add an un-mute command along with a volume up command from the control system.

- Program audio that is included in the EC ref may cause ducking when the level is set too high. Try setting the level so the meter reads -10 dB.

- Have an RS-232 to RJ-45 adapter set with you. Typically, you will be able to find a network cable that can be used to connect to the XAP system.

- For consistent setting of input levels, use pink noise as the reference source.

- Use isolated headphones to listen to what the system will sound like on the far-side of a conference call.

- The Min. and Max. tabs can be used to limit volume adjustment ranges.

- Use the AGC on gooseneck microphones.

- Do the calculations upfront in the planning stage to determine if the system will be intelligible.