TX-37A bid specifications

The transmitter operates in the 72–76MHz Auditory Assistance Band as approved by the FCC.  The transmitted field strength won’t exceed 80mV per meter at three meters. The operating frequency is digitally selectable by rear panel thumbwheel switches to any of 37 frequencies in the approved band. The transmitter is FCC and Industry Canada approved. Maximum FM deviation does not exceed a total of 50kHz. Frequency stability is controlled by a phaselocked loop frequency synthesizer with crystal reference and is accurate within ± 0.005% from 0–50° C. The transmitter has a 50Ω antenna connector for a local or remote antenna. The RF output level is adjustable by a rear panel slide switch providing 1/4, 1/2, and full power. The transmitter has XLR balanced and RCA unbalanced input jacks selectable as balanced mic, balanced and unbalanced line, and unbalanced speaker audio signals. There is a front panel control to adjust the audio input level with an LED audio level display. There is a switchable high-pass filter providing a 6dB/octave rolloff at 180Hz. There is an audio processing chain consisting of wide-band AGC, multi-band compression, Aphex Aural Exciter®, and peak limiting. There is a front panel control to regulate the overall amount of audio processing and a switchable 1kHz test tone to aid setup and receiver tuning. The transmitter is powered by an external AC line to 12VDC power adapter. The front panel has a power switch with LED and an LED to indicate proper RF carrier operation. There is a 1/4" stereo monitor jack with volume control. The transmitter is rack mountable in a standard 1 RU rack steel package. The TX37-A is specified.