PBL-310

#### LCD Projector Mount

## INSTALLATION  INSTRUCTIONS

# Step 1

Invert the projector and place it on a flat surface. Remove the back foot and locate the four (4) 4 (mm) mounting points found on the bottom of the projector. Align the mounting bracket to the projector and secure the mounting bracket with the four (4) 4 (mm) x 10 (mm) Phillip head screw (supplied)

See (F1)

Do not over tighten.

PREMIER LINE                    -_LA070301_-

- Step 1

Unpack the Gyrolock® Remove the upper and lower plates captured by the extension. Remove the two (2) 8 (mm) x 16 (mm)

hex screws on the top and lower portion on the Gyrolock®. Remove

the extension then connect the two plates together and re-install the

(2) 8 (mm) x 16 (mm) Allen screws. Do not over tighten screw.

Locate were the Gyrolock® would be installed. Secure the upper

plate with suitable hardware (commercially available) depending

on the installation requirements. Adjust the height desired by

loosening the two (2) 8 (mm) x 16 (mm) Allen screws found on the

extension post.

- Step 2

Raise the projector with the mounting bracket attached.

Insert the rotation plates tabs to the receiving tabs on the mounting

bracket. Once fully inserted rotate the projector 180,( align and

screw down the red safety screw. The screw must go past the arrow

shaped slot below to prevent further rotation. Screw

all the clamp screws to stabilize the mount. See (F2)

- Step 1

Locate were the Gyrolock® would be installed. Secure the upper

plate with suitable hardware (Commercially Available) depending on

the installation requirements. Adjust the height desired by loosening

two (2) 8 (mm) x 16 (mm) Allen screws found on the extension post.

- Step 2

Raise the projector with the mounting bracket attached.

Insert the rotation plates tabs to the receiving tabs on the mounting

bracket. Once fully inserted rotate the projector 180,( align and

screw down the red safety screw. The screw must go past the arrow

shaped slot below to prevent further rotation. Screw

all the clamp screws to stabilize the mount. See (F3)

- Step 1

Locate the wall were the Gyrolock® would be installed. Find the

wood stud behind the wall. Secure the Gyrolock® using suitable hardware (Commercially Available) depending on the installation requirements.

- Step 2

Raise the projector with the mounting bracket attached.

Insert the rotation plates tabs to the receiving tabs on the mounting

bracket. Once fully inserted rotate the projector 180,( align and

screw down the red safety screw. The screw must go past the arrow

shaped slot below to prevent further rotation. Screw

all the clamp screws to stabilize the mount. See (F4)

- Step 1

Locate were the Gyrolock® would be installed. Secure the upper

plate with (Commercially Available) Suitable hardware depending on

installation requirements. Remove the two (2) 8 (mm) x 16 (mm)

### Phillip Screws rotate the extension and insert it on the slot openings

reinstall the hardware. Follow previous Step 2.  See (F5)

### NOTE

Check all the hardware for proper tightness and security.

Do not over tighten hardware.

The wall/ceiling should be capable of supporting a weight of at least five (5) times the projector(s) or monitor(s)weight. If it cannot, the ceiling must be reinforced. Proper installation procedure by qualified personnel as outlined in the installation instructions must be adhered to. Failure to do so could result in serious personal injury.

DESCRIPTION/HARDWARE

A.    PBL-310 Mounting Bracket (1ea)

B.   4 (mm) x 10 (mm) Philip Screws (4ea)

- Projector (Not Included)

- Ceiling Structure

- Upper Plate

- Lag Bolts (Commercially available)

- Swivel Bracket (unit attached)

- Safety Screw

- Rotation Plates (unit attached)

- Anchor Screws

- Height Adjustable Screws

- Single Wood Stud

- Wall Structure

- Suspension Adapter

- PBL-UA Gyrolock® Assembly.

Note: If the height range required is grater than 12 ½” The (Optional) APS-2446 and the AST-2446 could be used

(Refer to the installations).

®

# Text boxes

For further information or ordering assistance

contact us at the phone/address number shown on the front of this page.