Sony MZ-M100 A top-notch little field recorder that captures uncompressed Linear PCM audio By Frank Moldstad

In an era when “MP3 quality” is not an oxymoron, it’s nice to see a portable audio device being marketed for its fidelity. Sony , which invented portable audio 25 years ago with the introduction of the Walkman, has just released its latest model, a top-notch little field recorder called the MZ- M100 (MSRP $439.95). It can record high-quality uncompressed PCM audio files onto Hi-MD removable discs, which come in 1GB capacities and cost about $7 apiece.

The Linear PCM capability and the small size (2 ¼ x 2 ¼-in. square) should make the MZ-M100 attractive to anyone seeking a high-quality mobile recorder that can transfer audio to a computer for editing. Among the potential users Sony has targeted for the MZ-M100 are recording engineers and journalists.

The MZ-M100 comes with a miniature stereo microphone , and includes an optical port for recording directly from digital playback devices. The optical port will also accept analog input via a mini-plug. There is a USB port for connecting to a computer, and software for transferring files on both Macs and PCs is provided – SonicStage for the PC and Hi-MD Wave Importer for the Mac (OS 10.2 and above).

The Mac software is designed for straightforward transfers from the recorder to the computer, automatically converting Linear PCM files to WAV format. That’s about all it does, although for importing mobile recordings, that is all it needs to do. The PC software is more versatile, allowing the transfer of MP3s, and use of the new Hi-MD ATRACS3plus format, a high-quality file compression scheme that the MZ-M100 can also record in that is 20 times the ratio of CD compression.

However, the MZ-M100 is recognized as a disc drive by both Macs and PCs, and it can be used for storage of data, images, and other files. I had no problem dragging and dropping MP3 files as well as JPEG files onto the MZ-M100 on a PC, and then opening them on a Mac.

Hi-MD 1GB disc

The 1GB Hi-MD disc will hold one hour and 34 minutes of Linear PCM files. Smaller capacity 80-minute MD discs can also be used, provided they are formatted on the MZ-M100.

One of the other important features of the MZ-M100 is its battery life. The recorder comes with a rechargeable nickel metal hydride battery that is able to record Linear PCM audio continuously for five and a half hours to a 1GB disc when fully charged. Battery recharging is done by plugging the MZ-M100 in with the provided power adapter, and pressing the charge button on the front of the recorder.

For more recording time, the MZ-M100 also comes with an AA alkaline dry battery case that snaps to the top of the recorder, providing an additional two hours. Using both batteries, the MZ-M100 is capable of recording continuously for eight hours. For technical reasons, there are slightly different recording times with the standard 60/74/80 minute standard discs. With both batteries, the standard discs are able to record up to nine and a half hours in the LinearPCM format.

Sony MZ-M100 A top-notch little field recorder that captures uncompressed Linear PCM audio The included Sony

ECM-DS 70P stereo mic

ECM-DS 70P stereo microphone is an electret condenser model that produces clear recordings with surprising separation for a uni-directional device. It should be suitable for most applications, but those who are recording music should be aware that the mic’s Frequency Response is 100-15,000Hz. If it’s important to capture the entire 20Hz-20kHz frequency range (which the recorder can do), it would be advisable to use a different mic.

The mic is powered through the stereo mini-jack, and the recorder has plenty of gain. Mic levels can be adjusted while recording by pressing the menu button and then using the jog  wheel to select REC Settings and from there MIC AGC. There are two options: Standard and For Loud Music. A similar procedure is used to adjust the mic sensitivity, selecting REC Settings and then MIC Sens to choose from Sens High or Sens Low options.

Actual recording levels are manually adjustable, but not while recording, which could get you into trouble if distortion occurs during a take. If this happens, the recorder needs to be put in standby mode while the jog wheel is used to lower the levels. Of course, the best thing to do is to get the levels right before you start. Sony recommends that the meter segments be set to light up around -12dB.

The meters and REC level settings are displayed with other menu information in a bright LCD window at the top left of the recorder. There are extensive options, but they are clearly organized. They include Edit, which has a Titler (with a full alphabet), Group Set/Release functionality, Move, Erase, and Format. In addition to Edit, other categories include Display settings, Play Mode, Sound (which has a six-band EQ), REC settings, a File List and Options.

To enter the Menu, you press and hold the Search/Light/Menu button in the middle of a crowd of tiny buttons on the right. It stands to reason that a tiny little recorder would have correspondingly small buttons, but the MZ-M100’s controls are not only small, they’re close together. Their tight proximity was no doubt chosen for design reasons (and the recorder does look good), but some people may find it difficult to access the rectangular ¼-in. long Record, Menu and Stop buttons. I found it easiest to depress them using the tip of my index finger, or even a fingernail. Fortunately, the jog wheel, which is the main navigational device through the Menu, can be easily scrolled with a thumb.

But while things like bigger buttons and changing levels while recording would enhance the usability, in the grand scheme of things they don't detract from the MZ-M100's mission, at which it succeeds brilliantly. It records uncompressed Linear PCM audio, and offloads it to a computer for editing. Plus, it's small enough to put in your pocket and offers up to eight hours of continuous recording on a battery. That's a compelling story. And, oh yeah, in your downtime you can plug in the included Earbuds and use it as a portable music player for downloadable tunes from Sony 's new Connect site (Windows only), or for MP3 files that you can drag and drop. Highly recommended.