ARCHITECT & ENGINEER SPECIFICATIONS

SECTION  16780

VIDEO SURVEILLANCE SYSTEMS

Model: EVT-820

8mm Time Lapse Recorder.

PART 2  PRODUCTS

2.01 CCTV TIME LAPSE VIDEO RECORDER SPECIFICATIONS

A. VIDEO - GENERAL REQUIREMENTS

1.   The Video Tape Recorder ( VTR )  shall utilize 8mm tape format.

2.   The recording system shall be rotary two (2) head, helical scanning still frame for high

resolution, noiseless

recording.

3.   The VTR shall feature six (6) user programmable time lapse recording modes. The time

modes shall be

12/24/48/96/192/760/ hour.

4.   The VTR shall feature alarm log, and alarm search capabilities.

5.   There shall be a programmable, position selectable,  time/date generator which shall

display month, day, year/hour,

minute and second in a shadow character format.

6.   To allow for series recording, the VTR shall feature Series Record In/Out terminals for

connection at additional

EVT-820 decks.

7.   The VTR shall provide a switch timing output (open collector) via BNC for connection

to external video switchers.

8.   The recorder shall feature a matrix, seven (7) day, twenty one (21) event  internal timer.

9.   To protect against unauthorized use or accidental system changes the VTR  shall feature

switchable (On/Off)

record lock.

10.  The VTR shall utilize Semiconductor Digital Memory for image storage and shall be

odd/even field selectable.

B. VIDEO - ELECTRICAL REQUIREMENTS

1.   The input voltage shall be AC 120 volts, 60 Hz.  Power consumption shall be 25 watts.

2.   The VTR shall have three (3) day power protection failure for time/date and record

mode.

3.   The signal system shall be EIA / NTSC standard for color video signals.

4.   The VTR shall produce a minimum 380 horizontal lines resolution , monochrome and

250 horizontal lines

resolution, color.

5.   The composite video input shall be 1.0 volt  peak to peak @ 75 Ohms, unbalanced via

BNC connector.

6.   The composite video output shall be 1.0 volt  peak to peak @ 75 Ohms,  unbalanced via

BNC connector.

7.   The signal to noise ratio shall be more than 45 dB in all recording modes.

8.   The approximate recording intervals for each record mode, with P6-90 tape, shall be - 12

hr/0.25  sec; 24 hr/0.5

sec; 48 hr/1.0 sec; 96 hr/2.0 sec; 192 hr/4.0 sec; 760 hr/16.0 sec.

9.   The erase system shall be Rotary Flying Erase  head.

10.  The VTR control system shall feature Pilot Signal ATF (Auto Track Finding) System.

The tracking system shall

be automatic.

11.  The fast forward/ rewind time with a P6-90 tape shall be approximately three (3)

minutes.

C. ALARM REQUIREMENTS

1.   The alarm record mode shall be activated by external devices by shorting the N.O. alarm

inputs terminals.

2.   The alarm recording speed shall be preset in the 12 hour mode.

3.   The alarm record duration shall be switchable from 10 seconds, 2 minutes or manual

mode.

D. MECHANICAL REQUIREMENTS

1.   For  rack mount accessibility  the VTR shall feature front panel tape loading.

2.   The recorder dimensions shall be 14"w x 3 1/2"h x 13 1/2"d  ( 355 x 86 x 340mm ) and

weigh 13lb. 14 oz

( 6.3 kg)

3.   The VTR  shall be capable of work station surface mounting or EIA standard 19" rack

mounting with optional rack

mount assembly.

E. ENVIRONMENTAL REQUIREMENTS

1.   The operating temperature shall be 41O F  to 104O F  (5O c to +40OC).  Operating

humidity shall be 35 percent to

80 percent,  non-condensing.

2.   The recorder will be suitable for indoor applications.  Proper ventilation and filtering

shall be required to maintain

operating temperature and air quality  when mounted in  equipment cabinets or  other

confined areas.

F. REFERENCES

1.   UL Listed 1409 - Low-Voltage Video Products Without Cathode-Ray-Tube Displays

2.   FCC Verified, Class A Digital Device

G. ACCESSORIES

1.   Supplied

a. 8-25CL Head Cleaning Tape

2.   Optional

a. MB-800 Rack Mount Kit - 2 units high (3.5")

b. SLR-800 Slide Rail Kit

c. P6-120MPB/A Tape

RELATED SECTIONS

Section  01540 - Construction Facilities and Temporary Controls: Security

Section  01650 - Facility Startup/Commissioning:  Administrative procedures for starting,

testing,  and

demonstrating systems

Section  02780 - Power and Communication: Electric Power Transmission,  Communication

Transmission

Section  02800 - Site Improvements:  Traffic controls

Section  11020 - Security and Vault Equipment:  Security and Emergency Systems

Section  11030 - Teller and Service Equipment:  Integration with teller systems.

Section  11052 - Library Equipment: Book Theft Protection

Section  11104 - Mercantile Equipment: Interfacing with cash register systems

Section  11130 - Audio-Visual Equipment:  Recorders,  and learning laboratories

Section  11150 - Parking Control Equipment

Section  11850 - Navigation Equipment

Section  13030 - Special Purpose Rooms: Shelters and booths, Vaults

Section  13800 - Building Automation Systems

Section  13950 - Special Security  Construction

Section  15950 - Controls

1995 Sony Broadcast Export Corp.  All rights reserved.  Feature and specifications subject to

change

without notice.  Non-metric weights and measurements are approximate. SONY, Remote

Commander, WatchCorder,

Hi8, Rotary Flying Erase and Nothing Escapes Us are trademarks of Sony.