ARCHITECT & ENGINEER SPECIFICATIONS

SECTION  16780

VIDEO SURVEILLANCE SYSTEMS

LCD-LC300

96 Hour - High Density VHS Time Lapse Recorder

PART  2	PRODUCTS

2.01	CCTV TIME LAPSE VIDEO RECORDER SPECIFICATIONS

A.	 VIDEO - GENERAL REQUIREMENTS

1.	The VTR (video tape recorder) shall utilize standard VHS tape format.

2.	The recording system shall be Dual Azimuth,  4-Head helical  scanning system.

3.	The VTR shall feature eight (8) user programmable time lapse recording modes. The program modes shall be dependent on the tape being used.

a.   The time modes with a T-120 tape shall be 6/18/30/48/72/96 hour.

b.   The time modes with a T-160 tape shall be 8/24/40/64/96/126 hour.

4. 	The VTR shall feature a menu driven, on screen display for programming system functions and unit status.  This shall be possible with or without an active video input.

5.   There shall be a programmable, position selectable,  time/date generator which shall display month, day, year, hour, minute and second in a shadow character format.

6.   For unattended continuous recording the VTR shall feature an automatic repeat record setting.  This function shall be automatically overridden in the event of an alarm.

7.   Extended Series recording shall be available by cascading multiple units together via series in and out terminals located on the rear panel.  When End of Tape is reached on the first unit, a series out signal is sent to the second unit to start recording.

8.   To allow for automatic program changes the recorder shall feature  seven (7) day,  eight (8) event internal timer capabilities.  For connection to external devices there shall be a + 5 volts TTL Level output that follows timer activations.

9.   The VTR shall provide a dry contact input terminal to allow recording start and stop via external equipment or timers.

10. The VTR shall have provisions to allow entry of up to 20 days, designated as non working days which shall follow the holiday record setting on the timer program.

11. The VTR shall provide a record check function that when activated shall rewind the tape for approximately three (3) seconds and playback the tape for approximately two (2)  	seconds.  The unit shall then return to its original record mode.

12. The VTR shall be capable of  forward field by field play back in the Still Mode.

13.	The VTR shall provide a  mini jack for connection of an external remote control device.

14.	The VTR shall feature automatic head cleaning.

15.	The VTR shall continually monitor the video signal integrity.  If a recording can not be made properly the unit shall activate the Clog Detection  warning.

16.	To protect against unauthorized use or accidental system changes the VTR  shall feature a programmable security lock feature.

B.   VIDEO - ELECTRICAL REQUIREMENTS

1.	The input voltage shall be AC 120 volts, 60 Hz.  Power consumption shall be 18 watts.

2.   The VTR shall have thirty (30) day power protection failure for time/date, record mode, record time and alarm programming.

3.   The signal system shall be EIA / NTSC standard for color video signals.

4.   The VTR shall produce a minimum 350 horizontal lines resolution, monochrome and 300 horizontal lines resolution, color.

5.   To obtain optimum picture performance the VTR shall feature Adaptive Picture Control (APC)  which automatically adjusts for the optimum video head bias based on the current condition of the tape and the video heads.

6.   The composite video input shall be 1.0 volt  peak to peak @ 75 Ohms, unbalanced via BNC connector.

7.   The VTR shall be capable of video signal loop through on power off mode, and E-E mode during normal power ON conditions.

8.   The signal to noise ratio shall be more than 43 dB (EP).

9.	The approximate recording intervals for each record mode shall be:

a.   T-120 tape: 6 hr/1/60 sec; 18 hr/1/20 sec; 30 hr/1/12 sec; 48 hr/0.15 sec; 72 hr/0.22 sec; 96 hr/0.28 sec.

b.   T-160 tape: 8 hr/1/60 sec; 24 hr/1/20 sec; 40 hr/1/12 sec; 64 hr/0.15 sec; 96 hr/0.22 sec;126 hr/0.28 sec.

10.	 A +5V, 5.7 k Ohm (active low) switch pulse output terminal shall be provided for interfacing with externally driven switchers, multiplexers or other devices.  Switch pulse output of the unit shall be field or frame selectable.  It shall be selectable for 1,2,3,4,5,10,30 or 60 Frame(s)/Field(s).

11.  A Clock Set input and output terminal shall be provided on the rear of the unit.  This shall allow multi-unit clock synchronization, which shall be updated once per day, specified to the hour by the end user.

12. The VTR shall feature an automatic Daylight  Savings Time clock function.  Activating the feature advances or reduces the time by one hour.

13. The recorder shall feature stationary erase head configuration.

14.	The fast forward/ rewind time with a T-120 tape shall be less than 2.5 minutes with a T-120 tape.

C.   AUDIO REQUIREMENTS

1.   Audio recording shall be available in the following modes:

a.   T-120: 6, 18, and 30 hour.

b.   T-160: 8, 24 and 40 hour.

2.   The audio input  shall be -7.8dBs @ 47 k Ohms via an phono style connector.

3.   The audio output shall be -7.8dBs  @ 600 Ohms via an phono style connector.

4.   The VTR shall provide a MIC input , -60dBs, 600 Ohm via a mini jack connector.

5.   Audio distortion shall be less than 4 percent.

6.   Audio signal to noise ratio shall be 40 dB.

D.   ALARM REQUIREMENTS

1. 	For alarm record mode activation from external devices the VTR shall provide a normally open, dry contact input via screw terminals.

2.   There shall be a +5  volts,  5.7k Ohms alarm output available via screw terminals for connection to external devices.  The alarm output shall follow alarm input activation, active low.

3.   The alarm recording speeds shall be programmable for 6 or 18 hour (T-120), 8 or 24 hour (T-160) and No Change.

4.   The VTR shall be fitted with a built-in buzzer which shall be activated during Alarm Recording or End of Tape.  This buzzer shall be capable of being manually activated/deactivated.

5.   The VTR shall have programmable alarm duration speeds of twenty (20) seconds, (40) seconds  1, 2, 3, 5 minutes, or follow the alarm activation period, or trigger mode.

6.  Trigger mode shall be provided as part of the alarm duration.  An alarm trigger of greater than 150  milliseconds shall activate the recorder into alarm recording until another trigger or reset signal is received, after which the unit shall go into the pause mode.

7.   An on-screen Alarm Recall log shall display the last eight (8) alarms by alarm count, month, day and time of occurrence, plus a running count of up to 999 alarm activations.

8.   To audit and select alarm activations for viewing,  the first five seconds of each alarm activation may be viewed via the Alarm Scan feature.

9.    Alarm Search shall be accomplished via the Alarm Recall and the Time/Date search feature.  For proper search operation to take place, the alarm record speed shall be in the 6 (8) hour mode, for 	a minimum duration of twenty seconds.

10.  A Warning Out signal shall be provided in the event recording is interrupted due to tape jam or clogged video heads.

11.  For signaling the end of the video tape a screw terminal output, +5 volts, 4.7 k Ohm signal shall be provided, active low.  The alarm buzzer shall also activate.

E.   MECHANICAL REQUIREMENTS

1.  The VTR shall feature front panel tape loading.

2.   The recorder dimensions shall be 9 1/2"w x 3 7/8"h x 13 1/8"d  ( 240 x 96.5 x 333 mm ) and 	weigh 8 lb.  6 oz.   (3.8 kg)

F.   ENVIRONMENTAL REQUIREMENTS

1.   The operating temperature shall be 41 degrees F  to 104 degrees F  (+5 degrees C to +40 degrees C).  Operating humidity shall be less than 80 percent,  non-condensing.

2.   The recorder will be suitable for indoor applications.  Proper ventilation and filtering shall  be required to maintain operating temperature and air quality  when mounted in equipment cabinets or  other confined areas.

G.   REFERENCES

1.   UL Listed 1409 - Low-Voltage Video Products Without Cathode-Ray-Tube Displays

2.   C-UL

3.   FCC  Class A

4.   IC Class A

H.   ACCESSORIES

1.   Optional

a.   SVT-RM10 Remote Control Unit

b.   T-120PM - 120 minute VHS Tape

c.   T-160VE - 160 minute VHS Tape

d.   SMB-240  19” Rack mount kit,  3 units high  (5.25”)

(1998 Sony Electronics Inc.  All rights reserved.  Features and specifications are subject to change without notice.  Non-metric weights and measurements are approximate.  SONY, Hyper Had, Trinitron, CCD-Iris and Nothing Escapes Us are trademarks of Sony.