ARCHITECT & ENGINEER SPECIFICATIONS

SECTION  16780

VIDEO SURVEILLANCE SYSTEMS

SPT-M124

General Purpose 1/3” Monochrome Camera

PART 2 	PRODUCTS

2.01   CCTV CAMERA SPECIFICATIONS

A.   VIDEO - GENERAL REQUIREMENTS

The camera shall utilize a 1/3" Hyper HAD   Interline Transfer CCD image sensor.  The image sensing  area shall be 4.4 mm x 3.3 mm utilizing 510h x 492v active picture elements. The camera shall produce 380 lines of horizontal  resolution.

The camera shall require a  minimum scene illumination of 0.1 lux at f/1.2,  89.9 percent reflectance.  To achieve  full video,  the scene illumination shall be 0.4  lux at f/1.2,  89.9 percent reflectance.

The camera shall have switchable (on/off) CCD Iris  control with a continuously variable range of  1/60th to 1/100,000th of a second.

The camera shall provide Backlight Compensation.  This shall be manually adjustable to the most suitable level within the range of the "Average" signal level, which detects the average brightness of  the image, and the "Peak" signal level, which detects the brightest part of the image.  The video "Level" adjustment, Low to High, shall allow further adjustment to achieve proper brightness in the area of  interest.

The camera shall accept both Video (ALC) or DC (Non-ALC) auto iris lenses.  This shall be accomplished through an externally accessible slide switch.

B. 	VIDEO - ELECTRICAL REQUIREMENTS

The input voltage shall be AC 24 volts ( 10 percent,  60 Hz  via screw type terminals.  Power consumption shall be  2.5 watts. The camera shall be electrically isolated from input power via isolation transformer in the DC to DC converter.

The scanning system shall be 525 lines,  60 fields/30 frames,  2:1 interlace.

The camera  shall have no geometric distortion.

Camera synchronization shall be external,   AC line lock 60 Hz,  with  ( 90 degrees Vertical Phase adjustment capability.

The camera shall have Automatic Gain Control (AGC).

The composite video output shall be 1.0 volt  peak to peak @ 75 Ohms,  sync negative via a BNC connector.

The signal to noise ratio shall be 45 dB minimum with AGC off.

C.	 MECHANICAL REQUIREMENTS

Lens mount shall be C or CS.  The camera shall utilize a precision double cam mechanism to accommodate the back focal length differences without  need for an 5 mm extension ring.  This shall be accomplished via a thumbwheel adjustment with lock screw.

Top or bottom camera mounting shall be obtained utilizing a removable plate with 1/4" x 20 mounting hole provided as a standard accessory. The mounting plate shall be 1/4 inch  (6.15 mm) in height.

The camera dimensions shall be 2 1/4"w x 2"h x 5 5/8"d  (57 x 50 x 115mm) and                         weigh 11 oz.  (320  grams)

D.	 ENVIRONMENTAL REQUIREMENTS

The operating temperature shall be 14 degrees F  to 122 degrees F  (-10 degrees C to +50 degrees C).  Operating humidity shall be 20 percent  to 80 percent ,  non-condensing.

The camera shall be suitable for indoor applications,  or outdoor applications with an approved, environmentally rated camera enclosure.

E.	REFERENCES

UL Listed 1492

FCC/IC  Verified Class B

(1998 Sony Electronics Inc.  All rights reserved.  Feature and specifications subject to change  without notice.  Non-metric weights and measurements are approximate. SONY, HyperHAD, CCD Iris and Nothing Escapes Us are trademarks of Sony.