ARCHITECT & ENGINEER SPECIFICATIONS

SECTION  16780

VIDEO SURVEILLANCE SYSTEMS

SSC-CX34

Integrated 1/3” Color Camera

with 12X Zoom Lens

PART 2  PRODUCTS

2.01 CCTV CAMERA SPECIFICATIONS

A. VIDEO - GENERAL REQUIREMENTS

The camera shall utilize a  high resolution  1/3" Hyper HAD  Interline Transfer CCD image sensor.  The image sensing area shall be 4.4 mm x 3.3 mm utilizing 768h x 494v active picture elements. The camera shall produce 470 lines horizontal resolution.

The camera shall require a  minimum scene illumination of 4.5 lux at f/1.8,  89.9 percent  reflectance. To achieve full video,  the scene illumination shall be 15 lux at f/1.8,  89.9 percent  reflectance.

The camera shall provide dip switch selectable (ON/OFF) backlight compensation. By utilizing digital signal processing with Smart Control( the camera shall provide automatic backlight  compensation independent of object positioning and shall require no set up or programming.

B.   OPTICAL  REQUIREMENTS

The camera shall have an internal 12X optical, auto iris motorized zoom lens.  The lens shall have a focal length of  5.4 mm to 64.8 mm and an aperture opening of  f1.8 to f2.7.

Lens functions, zoom, focus shall be controlled by conventional DC voltage method via a third party controller/receiver.

External manual lens control buttons shall also be available to control zoom (tele/wide) and focus (near/far).

The camera shall provide dip switch selectable iris modes of Auto Iris or Manual Iris.  Manual Iris Mode shall allow the lens iris to be controlled via a remote device or conventional receiver/driver.

The lens shall be capable of  zoom/focus preset/preposition  via external control device.

The lens control voltage shall be switch selectable for either 12V or 6V.  Voltage polarity shall be switch selectable for NORMAL or REVERSE operation.

C.  VIDEO - ELECTRICAL REQUIREMENTS

Input voltage shall be AC 24 volts ( 10 percent ,  60 Hz,  via screw terminals.  Power consumption shall  be 4.8 watts. The camera shall be electrically isolated from input power via isolation transformer in the DC to DC  converter.

The scanning system shall be 525 lines,  60 fields/30 frames,  2:1 interlace.

The camera shall have switch selectable white balance control with Auto Tracking White-Pro (ATW-Pro) or Auto Tracking White (ATW)

The ATW-Pro balance shall be accomplished by using absolute values referenced from the black body radiation curve and the color temperature of the scene.  The automatic adjustment range shall be 2,500 degrees K to 6,000 degrees K.

ATW shall extend the automatic adjustment range from 2,000 degrees K to 10,000       degrees K.

The camera shall also provide through the lens,  lockable Auto White Balance (AWB) which shall allow the camera to be manually locked on a specific color temperature via a white chart under desired lighting conditions.   This shall be selectable via a push button (lock).

The Auto White Balance range shall be from 2,000 degrees K to 10,000 degrees K.

The camera shall have no geometric distortion.

Camera synchronization  shall be switchable Internal or External AC line lock with  continuous vertical  phase adjustment via potentiometer covering ( 90 degrees.

The camera shall have switchable (on/off)  Automatic Gain Control (AGC).

The camera shall provide switchable (Normal/Turbo) Turbo AGC (  which shall allow for an additional 6 dB gain.

The composite video output shall be 1.0  volt  peak to peak  @ 75 Ohms,  sync negative via a BNC connector.

The signal to noise ratio shall be more than 50 dB with AGC off, Weight On.

D.	MECHANICAL REQUIREMENTS

Standard camera mounting shall be obtained utilizing 1/4" x 20 mounting  hole in the bottom of the camera body.  Top mounting is available via special mounting plate provided as a standard accessory.  The plate height shall be 3/8 inch ( 9.35 mm )

The camera dimensions shall be 2 3/8"w x 2 3/8"h x 5 1/8"d  (60 x 60 x 129.5 mm) and  weigh 1 lb. 2 oz. (520 grams)

E. 	ENVIRONMENTAL REQUIREMENTS

The operating temperature shall be 14 degrees  F  to 122 degrees F  (-10 degrees C to +50 degrees C).   Operating humidity shall be 20 percent  to 80 percent,  non-condensing.

The camera will be suitable for indoor applications,  or outdoor applications with an approved  environmentally rated camera enclosure.

F.	 REFERENCES

UL Listed 1492 - Low-Voltage Video Products Without Cathode-Ray-Tube Displays

FCC Verified  Class B Digital Device

(1997 Sony Electronics Inc.  All rights reserved.  Feature and specifications subject to change without notice.  Non-metric weights and measurements are approximate. SONY, HyperHAD, CCD Iris, Smart Control and Nothing Escapes Us are trademarks of Sony.