ARCHITECT & ENGINEER SPECIFICATIONS

SECTION  16780

VIDEO SURVEILLANCE SYSTEMS

SSC-DC50/54

High Resolution ½” Digital Color Camera

PART 2	 PRODUCTS

2.01	CCTV CAMERA SPECIFICATIONS

A.	VIDEO - GENERAL REQUIREMENTS

1.   The camera shall utilize a  high resolution  1/2" Hyper HAD   Interline Transfer CCD 	image sensor.  	The image sensing area shall be  6.3 mm x 4.7 mm utilizing 768h x 494v 	active picture elements. 	The camera shall produce 470 lines horizontal resolution.

2.   The camera shall require a  minimum scene illumination of 1.9 lux at f/1.2,  89.9 percent  	reflectance, Turbo AGC ON.  To achieve full video,  the scene illumination shall be 6.5 	lux at 	f/1.2,  89.9 percent  reflectance.

3.   The camera shall provide switch selectable (ON/OFF) backlight compensation. By 	utilizing 	digital signal processing with Smart Control the camera shall provide automatic 	backlight  	compensation independent of object positioning and shall require no set up or 	programming.

4. 	An Auto Exposure mode shall be available to allow backlight optimization of specific 	target 	areas.  The AE mode shall feature seven (7)  selectable preset target areas available 	via rotary 	selector. ( DC type auto iris lens or CCD Iris  mode only)

5.  	The camera shall have four (4) modes of white balance. ATW PRO, ATW, AWB and 	Preset 5600 	degrees K.

6.   The camera shall have a continuously variable CCD Iris  with a control range of 1/60th  	to  	1/100,000th second.

7.   The camera shall have 8 selectable shutter speeds from 1/60th  to  1/10,000th  second.  	This shall 	be accomplished via externally accessible rotary selector.

8.   The camera shall have a switch selectable aperture setting for Normal or Sharp modes.

9.   The camera shall accept both Video (ALC) or DC (Non-ALC) auto iris lenses. This shall 	be 	accomplished through an externally accessible slide switch.

B.	VIDEO - ELECTRICAL REQUIREMENTS

1.   (SSC-DC50)

The input voltage shall be DC 12 volts via screw  terminals,  or DC multiplex power over 	coax of 	24 volts ( 5 volts via the optional YS-W150 or YS-W250 camera adapters.  	Power consumption 	shall be 4.5 watts DC 12 volts and 5.5 watts with the camera 	adapters.  The camera shall have an 	external ON/OFF power switch.  However,  		camera power control (on/off) shall be 		accomplished through the power switch of 	the 	camera adapters regardless of  the external on/off 	switch setting on the camera        	when used with the YS-W150/250 power adapters only.

1.   (SSC-DC54)

Input voltage shall be AC 24 volts ( 10 percent ,  60 Hz,  via screw terminals.  Power 	consumption 	shall  be 6.0  watts. The camera shall be electrically isolated from 	input 	power via isolation 	transformer in the DC to DC  converter.

2.   The scanning system shall be 525 lines,  60 fields/30 frames,  2:1 interlace.

3.   The camera shall have switch selectable white balance control with Auto Tracking 	White-Pro 	(ATW-Pro) or Auto Tracking White (ATW).

4.   The ATW-Pro balance shall automatically adjust between the ranges of  2,500 	degrees K to 	6,000 degrees K.

5.   ATW shall extend the automatic adjustment range from 2,000 degrees K to 10,000 	degrees K.

6.	The camera shall also provide through the lens,  lockable Auto White Balance (AWB) 	which 	shall allow the camera to be manually locked on a specific color temperature 	via 	a white chart 	under desired lighting conditions.   This shall be selectable via a 	push 	button (lock).

7.	The Auto White Balance range shall be from 2,000 degrees K to 10,000 degrees K.

8 .	The camera shall provide a preset color temperature rating of  5600 degrees K.

9.   The camera shall have no geometric distortion.

10. (SSC-DC50)

Camera synchronization shall be internal or external.  External sync shall be automatic 	switchover 	upon sensing an external synchronizing signal.  Camera shall accept 	Composite Sync ( 4 volts  	peak to peak),  VS (1  volt  peak to peak) or VBS (1	volt  	peak to peak ) external synchronization 	and shall have a horizontal phase adjustment 	range of ( 0.12H.  The camera shall be capable of 	accepting external sync over coax (VS) 	via the optional  power adaptors YS-W150 or YS-W250.

10. (SSC-DC54)

Camera shall be capable of internal or external synchronization.  External  	synchronization shall 	either be 60 Hz AC Line Lock with ( 90 degree V-Phase 	adjustment, or VS and VBS via the 	external sync BNC.

11.	The camera shall have a 180 degree phase reversal switch (course adjustment) and a  ( 90 				degree sub-carrier fine adjustment potentiometer.

12. The camera shall have switchable (on/off)  Automatic Gain Control (AGC).

13. The camera shall provide switchable (Normal/Turbo) Turbo AGC( which shall allow 	for an 	additional 6 dB gain.

14. (SSC-DC50)

The video output shall be 1.0 volt  peak to peak  @ 75 Ohms,  sync negative.  This output shall be 	obtained on the following Mode Select setting on the camera:

a. 	MODE A (with YS-W150/250) - MONITOR OUT/VS IN  BNC Connector Video out 1 		or 2 of YS-W150/250.

b.	 MODE B  ( DC  12 volts ) - DC IN/VS IN/VIDEO OUT BNC Connector.

14. (SSC-DC54)

The composite video output shall be 1.0  volt  peak to peak  @ 75 Ohms,  sync negative 	via a BNC 	connector.

15.	The camera shall also provide S-Video (Y/C) output.  Luminance (Y) shall be 1.0Vp-p, 	75  Ohm, 	sync negative, Chrominance (C) shall be 0.286Vp-p, 75 Ohm, sync negative.

16. The signal to noise ratio shall be 50 dB with AGC off, Weight On.

C. 	MECHANICAL REQUIREMENTS

1.   Lens mount shall be C or CS.  The camera shall utilize a precision double cam 	mechanism to  	accommodate the back focal length differences without  need for an 5 mm 	extension ring.  Fine 	focus  shall be accomplished via an adjustment ring for image sensor  	back focus with a lock down 	screw.

2.   Top or bottom camera mounting shall be obtained utilizing a removable plate with 1/4" x 	20 mm 	mounting holes provided.  The plate height shall be 3/8 inch ( 9.35 mm )

3.   The camera dimensions shall be 2 7/8"w x 2 1/4"h x 5 1/8"d  (64 x 57 x 137 mm) and  	weigh 1 lb. 	5 oz. (600 grams)

D. 	ENVIRONMENTAL REQUIREMENTS

1.   The operating temperature shall be 14 degrees  F  to 122 degrees  F  (-10 degrees C to 	+50 	degrees C).   Operating humidity shall be less than 80 percent,  non-condensing.

2.   The camera will be suitable for indoor applications,  or outdoor applications with an 	approved  	environmentally rated camera enclosure.

E. 	REFERENCES

1.   UL Listed 1492 - Low-Voltage Video Products Without Cathode-Ray-Tube Displays

2.   FCC Verified  Class B Digital Device

F. 	ACCESSORIES

1. 	YS-W150 - Single camera adaptor:  Provides power/sync/video multiplexing via single 	coaxial 	cable  and two (2) isolated video outputs.

a. Video Input/DC Output :   	BNC X1

b. Video Output:    			BNC X2

c. Sync Mode:   				Line Lock, Internal, or external

d  Sync Input:    				BNC X1

e. Sync Output:    				BNC X1

f. Power Requirements:   		AC 120 volts,  50/60 Hz

g. Power Consumption:    		15 watts

h. Maximum Cable Length:    1000 ft. using RG-59B/U

1500 ft. using RG-6A/U

2000 ft. using RG-11A/U

2.   YS-W250 - Four Camera Adapter:  Provides power/sync/video multiplexing via single 	cable for 	four  (4) cameras and two (2) isolated video outputs per camera.

a. Video Input/DC Output :    BNC X4

b. Video Output:   			BNC X8  (2 outputs per camera)

c. Sync Mode:    				Line Lock, Internal, or External

d. Sync Input:    				BNC X1

e. Sync Output:    				BNC X1

f. Power Requirements:    		AC 120  volts,  50/60 Hz

g. Power Consumption:    		65 watts

h. Maximum Cable Length:    1000 ft. using RG-59B/U

1500 ft. using RG-6A/U

2000 ft. using RG-11A/U

(1997 Sony Electronics Inc.  All rights reserved.  Feature and specifications subject to change without notice.  Non-metric weights and measurements are approximate. SONY, HyperHAD, CCD Iris, Smart Control and Nothing Escapes Us are trademarks of Sony.