ARCHITECT & ENGINEER SPECIFICATIONS

SECTION  16780

VIDEO SURVEILLANCE SYSTEMS

#### Model: SSC-DC50A/54A

High Resolution ½” Digital Color Camera

# PART 2	 PRODUCTS

2.01	CCTV CAMERA SPECIFICATIONS

A.	VIDEO - GENERAL REQUIREMENTS

1.   The camera shall utilize a high resolution 1/2" EXWAVE HAD( Interline Transfer CCD image sensor.  The image sensing area shall be 6.3 mm x 4.7 mm utilizing 768h x 494v active picture elements.  The camera shall produce 470 lines horizontal resolution.

2.   The camera shall require a minimum scene illumination of 0.4 lux at f/1.2, 89.9 percent reflectance,                                         Turbo AGC ON (30 IRE); or 0.8 lux at 50 IRE.  To achieve full video, the scene illumination shall be 3.0 lux at f/1.2, 89.9 percent reflectance.

3.	The camera shall have a smear level of –120 dB.

4.   The camera shall provide switch selectable (ON/OFF) backlight compensation.  By utilizing digital signal processing with Smart Control the camera shall provide automatic backlight compensation independent of object positioning and shall require no set up or programming.

5. 	An Auto Exposure mode shall be available to allow backlight optimization of specific target areas.  The AE mode shall feature seven (7) selectable preset target areas available via rotary selector.  (DC type auto iris lens or CCD Iris mode only)

6.  	The camera shall have four (4) modes of white balance.  ATW PRO, ATW, AWB and Preset 5600 degrees K.

7.   The camera shall have a continuously variable CCD Iris with a control range of 1/60th to 1/100,000th second.

8.   The camera shall have eight (8) selectable shutter speeds from 1/60th to 1/10,000th second.  This shall be accomplished via externally accessible rotary selector.

9.   The camera shall have a switch selectable aperture setting for Normal or Sharp modes.

10. The camera shall accept both Video (ALC) or DC (Non-ALC) auto iris lenses.  This shall be accomplished through an externally accessible slide switch.

### B.	VIDEO - ELECTRICAL REQUIREMENTS

1.   (SSC-DC50A)

The input voltage shall be a DC 12 volt via screw terminals, or DC multiplex power over coax of 24 volts ( 5 volts via the optional YS-W150 or YS-W250 camera adapters.  Power consumption shall be 4.5 watts DC 12 volts and 5.5 watts with the camera adapters.  The camera shall have an external ON/OFF power switch.  However, camera power control (on/off) shall be accomplished through the power switch of the camera adapters regardless of the external on/off switch setting on the camera when used with the YS-W150/250 power adapters only.

1.   (SSC-DC54A)

Input voltage shall be AC 24 volts ( 10 percent, 60 Hz, via screw terminals.  Power consumption shall be 6.0 watts. The camera shall be electrically isolated from input power via an isolation transformer in the DC to DC converter.

2.   The scanning system shall be 525 lines, 60 fields/30 frames, 2:1 interlace.

3.   The camera shall have switch selectable white balance control with Auto Tracking White-Pro (ATW-Pro) or Auto Tracking White (ATW).

4.   The ATW-Pro balance shall automatically adjust between the ranges of 2,500 degrees K to 6,000 degrees K.

5.   ATW shall extend the automatic adjustment range from 2,000 degrees K to 10,000 degrees K.

6.	The camera shall also provide through the lens, lockable Auto White Balance (AWB) 	which shall allow the camera to be manually locked on a specific color temperature via a white chart under desired lighting conditions.  This shall be selectable via a push button (lock).

7.	The Auto White Balance range shall be from 2,000 degrees K to 10,000 degrees K.

8.	The camera shall provide a preset color temperature rating of 5600 degrees K.

9.   The camera shall have no geometric distortion.

10. (SSC-DC50A)

Camera synchronization shall be internal or external.  External sync shall be automatic switchover upon sensing an external synchronizing signal.  Camera shall accept Composite Sync (4 volts peak to peak), VS (1 volt peak to peak) or VBS (1 volt peak to peak) external synchronization and shall have a horizontal phase adjustment range of ( 0.12H.  The camera shall be capable of accepting external sync over coax (VS) via the optional power adapters YS-W150 or YS-W250.

10. (SSC-DC54A)

Camera shall be capable of internal or external synchronization.  External synchronization shall either be 60 Hz AC Line Lock with ( 90 degree V-Phase adjustment, or VS and VBS via the external sync BNC.

11.	The camera shall have a 180-degree phase reversal switch (coarse adjustment) and a ( 90-degree sub-carrier fine adjustment potentiometer for genlock.

12. The camera shall have switchable (on/off) Automatic Gain Control (AGC).

13. The camera shall provide switchable (Normal/Turbo) Turbo AGC( that shall allow for an additional 6-dB gain.

14. (SSC-DC50A)

The video output shall be 1.0-volt peak to peak  @ 75 Ohms, sync negative.  This output shall be obtained on the following Mode Select setting on the camera:

a. 	MODE A (with YS-W150/250) - MONITOR OUT/VS IN BNC Connector Video Out 1 or 2 of YS-W150/250.

b.	 MODE B  (DC 12 volts) - DC IN/VS IN/VIDEO OUT BNC Connector.

14. (SSC-DC54A)

The composite video output shall be 1.0-volt peak to peak  @ 75 Ohms, sync negative via a BNC connector.

15.	The camera shall also provide S-Video (Y/C) output.  Luminance (Y) shall be 1.0Vp-p, 75 Ohm, sync negative, Chrominance (C) shall be 0.286Vp-p, 75 Ohm, sync negative.

16. The signal to noise ratio shall be 50 dB with AGC off, Weight On.

## C. 	MECHANICAL REQUIREMENTS

1.   Lens mount shall be C or CS.  The camera shall utilize a precision double cam mechanism to accommodate the back focal length differences without need for a 5-mm extension ring.  Fine focus shall be accomplished via an adjustment ring for image sensor back focus with a lock down 	screw.

2.   Top or bottom camera mounting shall be obtained utilizing a removable plate with 1/4" x 	20 mm mounting holes provided.  The plate height shall be 3/8 inch (9.35 mm).

3.   The camera dimensions shall be 2 7/8"w x 2 1/4"h x 5 1/8"d  (64 x 57 x 137 mm) and weigh 1 lb. 5 oz. (600 grams).

## D. 	ENVIRONMENTAL REQUIREMENTS

1.   The operating temperature shall be 14 degrees F to 122 degrees F  (-10 degrees C to +50 degrees C).  Operating humidity shall be less than 80 percent, non-condensing.

2.   The camera will be suitable for indoor applications, or outdoor applications with an 	approved environmentally rated camera enclosure.

## E. 	REFERENCES

1.   UL Listed 1492 - Low-Voltage Video Products without Cathode-Ray-Tube Displays

2.   FCC Verified Class B Digital Device

### F. 	ACCESSORIES

1. 	YS-W150 - Single camera adaptor: Provides power/sync/video multiplexing via single coaxial cable and two (2) isolated video outputs.

a. 	Video Input/DC Output: 	BNC X1

b. 	Video Output: 				BNC X2

c. 	Sync Mode: 				Line Lock, Internal, or external

d.  	Sync Input:    				BNC X1

e. 	Sync Output: 				BNC X1

f. 	Power Requirements: 		AC 120 volts, 50/60 Hz

g. 	Power Consumption: 		15 watts

h. 	Maximum Cable Length: 	1000 ft. using RG-59B/U

1500 ft. using RG-6A/U

2000 ft. using RG-11A/U

2.   YS-W250 - Four-Camera Adapter: Provides power/sync/video multiplexing via single cable for four  (4) cameras and two (2) isolated video outputs per camera.

a. 	Video Input/DC Output:   BNC X4

b. 	Video Output: 				BNC X8  (2 outputs per camera)

c. 	Sync Mode:    				Line Lock, Internal, or External

d. 	Sync Input:    				BNC X1

e. 	Sync Output:    			BNC X1

f. 	Power Requirements:    	AC 120  volts,  50/60 Hz

g. 	Power Consumption:    	65 watts

h. 	Maximum Cable Length: 1000 ft. using RG-59B/U

1500 ft. using RG-6A/U

2000 ft. using RG-11A/U