ARCHITECT & ENGINEER SPECIFICATIONS

SECTION  16780

VIDEO SURVEILLANCE SYSTEMS

SSC-M254/256

1/2” Monochrome Camera

PART 2  PRODUCTS

2.01 CCTV CAMERA SPECIFICATIONS

A. VIDEO - GENERAL REQUIREMENTS

1.   The camera shall utilize a 1/2" Hyper HAD    Interline Transfer CCD image sensor.  The

image sensing area shall be  6.3 mm x 4.7 mm utilizing 510h x 492v active picture elements. The

camera shall produce 380 lines horizontal  resolution.

2.   The camera shall require a  minimum scene illumination of  0.3 lux at f/1.2,  89.9 percent

reflectance.  To achieve full video,  the scene illumination shall be 2.47* lux at f/1.2,  89.9 percent

reflectance.

3.   The camera shall have an internal switch to enable or disable the 8 step  electronic iris

control.

4.   The  electronic iris control range shall be 1/60th to 1/10,000th of a second.

5.   The camera shall accept Video (ALC) type auto iris lenses.

B. VIDEO - ELECTRICAL REQUIREMENTS

1.   ( SSC-M254)

The input voltage shall be AC 24 volts + 10 percent,  60 Hz via screw type terminals.

Power consumption shall be 4.5 watts. The camera shall be electrically isolated from input power

via isolation transformer.

1.   ( SSC-M256)

Input voltage  shall be AC 120  volts + 10 percent,  60 Hz .  It shall have 3-prong grounded

plug.  The camera shall have an external on/off power  switch.  Power consumption shall be 4.5

watts.  The camera shall be electrically isolated from input power via isolation transformer.

2.   The scanning system shall be 525 lines,  60 fields/30 frames,  2:1 interlace.

3.   The camera  shall have no geometric distortion.

4.   Camera synchronization shall be external,   AC line lock 60 Hz,  with  + 90 degrees

Vertical Phase adjustment capability.

5.   The camera shall have Automatic Gain Control (AGC).

6.   The composite video output shall be 1.0 volt peak to peak @ 75 Ohms,  sync negative

via a BNC connector.  The signal to noise ratio shall be 48 db minimum  with AGC off.

*  Due to Knee Circuit.

C. MECHANICAL REQUIREMENTS

1.   The camera may utilize either  CS,  or,  C mount lenses with the supplied 5 mm ring

adapter.  Fine focus shall be accomplished via a recessed screw  for image sensor back focus

adjustment.

2.   To allow for flexibility of mounting 1/4" x 20 mounting holes will be available on the top

and bottom of the camera chassis.

3.   The camera dimensions shall be 2 1/2"w x 2 1/8"h x 6"d  (64 x 53 x 150 mm) and weigh

(M254) 1 lb. 12 oz. (800 grams);  (M256)  2 lbs. 2 oz.  (990 grams)

D. ENVIRONMENTAL REQUIREMENTS

1.   The operating temperature shall be 14 degrees F  to 122 degrees F  (-10 degrees C to

+50 degrees C).  Operating humidity shall be 20 percent to 80 percent,  non-condensing.

2.   The camera shall be suitable for indoor applications,  or outdoor applications with an

approved environmentally rated camera enclosure.

E. REFERENCES

1.   UL Listed 1409 - Low-Voltage Video Products Without Cathode-Ray-Tube Displays

2.   CSA Listed C22.2 # 1 (SSC-M256 Only)

3.   FCC Verified  Class A Digital Device

( 1995 Sony Electronics, Inc.  All rights reserved.  Feature and specifications subject to change without notice.  Non-metric weights and measurements are  approximate. SONY, HyperHAD, CCD Iris and Nothing Escapes Us are trademarks of Sony.