ARCHITECT & ENGINEER SPECIFICATIONS

SECTION  16780

VIDEO SURVEILLANCE SYSTEMS

Models: SSC-M370/374

High Resolution 1/2” Monochrome Camera

PART 2  PRODUCTS

2.01 CCTV CAMERA SPECIFICATIONS

A. VIDEO -GENERAL REQUIREMENTS

1.   The camera shall utilize a high resolution 1/2" Hyper HAD    Interline Transfer CCD image sensor.  The image sensing area shall be  6.3 mm x 4.7 mm utilizing 768h x 494v active picture elements. The              camera shall produce 570 lines horizontal  resolution.

2.   The camera shall require a  minimum scene illumination of  0.3 lux at f/1.2,  89.9 percent reflectance.               To achieve full video,  the scene illumination shall be .57 lux* at f/1.2,  89.9 percent reflectance.

3.   The camera shall have a continuously variable CCD Iris  with a control range of 1/60th  to  1/100,000th second.

4.   The camera shall have 8 selectable shutter speeds from 1/60th  to  1/10,000th  second.

5.   An external 4-pin connector will be provided for VIDEO Type auto iris lenses.

B. VIDEO - ELECTRICAL REQUIREMENTS

1.    (SSC-M370)

The input voltage shall be DC 12 volts via screw  terminals,  or DC multiplex power over coax of DC           24 volts + 5 volts via the optional YS-W150 or YS-W250 camera adapters.  Power consumption shall           be 2.8 watts  DC 12  volts and 4.0 watts with the camera adapters.  The camera shall have an external           ON/OFF power switch.  However,  camera power control (on/off) shall be accomplished through the           power switch of the camera adapters regardless of  the external on/off switch setting on the camera           when used with the YS-W150/250 power adapters only.

1.   (SSC-M374)

Input voltage   shall be AC 24 volts + 10 percent,  60 Hz,  via screw terminals.  Power consumption           shall be 3.9 watts.  The camera shall have an external power ON/OFF switch located on the rear of the           camera.  The camera shall be electrically isolated from input power via isolation transformer in the DC           to DC converter.

2.   The scanning system shall be 525 lines,  60 fields/30 frames,  2:1 interlace.

3.   The camera  shall have no geometric distortion.

4.    (SSC-M370)

Camera synchronization shall be internal or external.  External sync shall be automatic switchover upon           sensing an external synchronizing signal.  Camera shall accept Composite Sync ( 4  volts  peak to peak),           VS (1.0 volt  peak to peak) or VBS (1.0 volt  peak to peak) external synchronization and shall have a                     horizontal phase adjustment range of + 8 sec.  The camera shall be capable of accepting external sync                     over coax (VS)  via the optional power adaptors YS-W150 or YS-W250.

4.   (SSC-M374)

Camera synchronization  shall be switchable Internal or External AC line lock with vertical phase           adjustment via push button switches in + 60 degree  increments, to cover the full 360 degrees.

5.   The camera shall have switchable (on/off)  Automatic Gain Control (AGC).

6.   (SSC-M370

The video output  shall be 1.0 volt  peak to peak @ 75 Ohms,  sync negative.  This output shall be           obtained on the following Mode Select setting on the camera:

a. MODE A (with YS-W150/250)  -  MONITOR OUT/VS IN  BNC Connector                                              Video out 1 or 2 of YS-W150/250

b. MODE B  ( DC  12  volts ) -  DC IN/VS IN/VIDEO OUT BNC Connector

6.   (SSC-M374)

The composite video output  shall be 1.0 volt  peak to peak @ 75 Ohms,  Sync negative via a BNC              connector.

7.   The signal to noise ratio shall be 50 db with AGC off.

C. MECHANICAL REQUIREMENTS

1.   The camera shall accept C-mount lenses.  Fine focus shall be accomplished via a recessed screw  for              image sensor back focus adjustment.

2.   To allow for flexibility of mounting, 1/4" x 20 mounting holes will be available on the top and bottom              of the camera chassis.

3.   The camera dimensions shall be 2 5/8"w x 2 1/4"h x 61/8"d  (64 x 57 x 155 mm) and weigh  1 lb. 7 oz.               (660 grams)

D. ENVIRONMENTAL REQUIREMENTS

1.   The operating temperature shall be 14 degrees  F  to 122 degrees  F  (-10 degrees  C to +50 degrees ). Operating humidity shall be 20 percent to 80 percent,  non-condensing.

2.   The camera shall be suitable for indoor applications,  or outdoor applications with an approved              environmentally rated camera enclosure.

E. REFERENCES

1.   UL Listed 1409 - Low-Voltage Video Products Without Cathode-Ray-Tube Displays

2.   FCC Verified Class A Digital Device

F. ACCESSORIES

1.   YS-W150 - Single camera adaptor:  Provides power/sync/video multiplexing via single coaxial cable               and two (2) isolated video outputs.

a. Video Input/DC Output:    	BNC X1

b. Video Output:    			BNC X2

c. Sync Mode:    				Line Lock, Internal, or external

d  Sync Input:    				BNC X1

e. Sync Output:    				BNC X1

f. Power Requirements:    		AC 120 volts,  50/60 Hz

g. Power Consumption:    	15 watts

h. Maximum Cable Length:    1000 ft. using RG-59B/U

1500 ft. using RG-6A/U

2000 ft. using RG-11A/U

2.   YS-W250 - Four Camera Adapter:  Provides power/sync/video multiplexing via single cable for four              (4) cameras and two (2) isolated video outputs per camera.

a. Video Input/DC Output :    BNC X4

b. Video Output:    			BNC X8  (2 outputs per camera)

c. Sync Mode:    				Line Lock, Internal, or External

d. Sync Input:    				BNC X1

e. Sync Output:   				BNC X1

f. Power Requirements:    		AC 120  volts,  50/60 Hz

g. Power Consumption:    	65 watts

h. Maximum Cable Length:    1000 ft. using RG-59B/U

1500 ft. using RG-6A/U

2000 ft. using RG-11A/U

( 1996 Sony Electronic Inc.  All rights reserved.  Feature and specifications subject to change without notice.  Non-metric weights and measurements are approximate.  SONY, HyperHAD, CCD Iris and Nothing Escapes Us are trademarks of Sony.