ARCHITECT & ENGINEER SPECIFICATIONS

SECTION  16780

VIDEO SURVEILLANCE SYSTEMS

SSM-125

12" Monochrome Monitor

PART	2  PRODUCTS

2.01	 CCTV MONITOR SPECIFICATIONS

A.	VIDEO - GENERAL REQUIREMENTS

1.   The monitor shall be  black and white (monochrome) measuring 12" diagonally - 90 degree deflection.

2.   The monitor shall be capable of work station surface mounting or EIA standard 19" rack mounting with optional rack mount assembly.

B.	VIDEO - ELECTRICAL REQUIREMENTS

1.   The input voltage shall be AC 120 volts,  60 Hz.  Power consumption shall be approximately 30 watts.

2.   The signal system shall be EIA Monochrome Standard.

3.   The horizontal resolution at center shall be more than 750 lines.

4.   The horizontal linearity shall be less than 11 percent.  The vertical linearity shall be less than 8 percent.

5.   The brightness at high light setting with all white picture signal shall be 200 nt plus or minus 50 nt.

6.   The monitor shall have two  composite video inputs labeled   A & B.  Each input shall be 0.5 to 2.0 volts peak to peak @ 75 Ohms, sync negative via BNC connectors.  Video input viewing shall be selectable,  A/B,  through front push button controls.

7.  The monitor shall have  switch selectable (On/Off)  75 Ohm termination or high impedance composite video loop through available for connection to external devices via BNC connector.

8.  The monitor shall have switch selectable (On/Off) DC Clamp for stable black level reference.

C. 	MECHANICAL REQUIREMENTS

1.   The monitor dimensions shall be 11 3/4"w x 12"h x 11 7/8"d ( 296 x 303 x 301 mm) and weigh 20 lb. 5 oz. (9.2 kg)

2.   Front panel controls shall feature push button On/Off, Video Input A/B,  and rotary Horizontal Hold, Vertical Hold,  Brightness and  Contrast controls.

3.   Rear panel controls shall feature slide switch selectable On/Off  75 Ohm termination for A & B video inputs, DC Clamp and recessed screw adjustments for Vertical Height and Vertical Linearity.

D. ENVIRONMENTAL REQUIREMENTS

1.   The operating temperature shall be  32 degrees F  to 95 degrees F (0 degrees C to +35 degrees C).  Operating humidity shall be 20 percent to 80 percent,  non-condensing.

2.   The monitor will be suitable for indoor applications.  Proper ventilation shall be required to maintain operating temperature  when mounted in  equipment cabinets or  other confined areas.

E. 	REFERENCES

1.   UL Listed 1410 - Television Receivers and High Voltage Video Products

2.   C-UL

3.	FCC  Class A

4.	IC Class A

F. 	ACCESSORIES

1.   Optional

a. 	SMB - 121 - 19" rack mount adapter for single SSM-125 configuration.  Rack kit  height is 7 rack units  ( 12.25")

(1998 Sony Electronics Inc.  All rights reserved.  Features and specifications are subject to change without notice.  Non-metric weights and measurements are approximate.  SONY, Hyper Had, Trinitron, CCD-Iris and Nothing Escapes Us are trademarks of Sony.