ARCHITECT & ENGINEER SPECIFICATIONS

SECTION  16780

VIDEO SURVEILLANCE SYSTEMS

Models: SSM-14/20 N1U

14” & 20” Color Monitor

PART 2  PRODUCTS

2.01 CCTV MONITOR SPECIFICATIONS

A. VIDEO - GENERAL REQUIREMENTS

1.   ( SSM-14N1U )

The monitor shall be  color,  with a 13 inch diagonal viewing area.

1 .  ( SSM-20N1U )

The monitor shall be  color,  with a 19 inch diagonal viewing area.

2.   The monitor shall have on screen menu programming.

3.   The monitor shall be capable of work station surface mounting or EIA standard 19" rack mounting              with optional rack mount assembly.

B. VIDEO - ELECTRICAL REQUIREMENTS

1.   The input voltage shall be AC 100 to 240 volts, 50/60 Hz.

2.   ( SSM-14N1U)

Power consumption shall be 80 watts maximum.

2.   ( SSM-20N1U )

Power consumption shall be 100 watts maximum.

3.   The signal system shall be EIA and the color standard shall be NTSC/PAL/SECAM/NTSC 4.43.

4.   The horizontal resolution at center shall be 500 lines.

5.   The monitor shall have a color temperature rating of 6500 degrees K.

6.   The monitor shall provide one (1)composite video input.  The input shall be 1.0 volt peak to peak @              75 Ohms, sync negative via BNC connectors.

7.   There shall be an  S-Video (Y/C) input, Y (Luminance) 1.0 volt peak to peak @ 75 Ohm, sync negative, C (Chrominance) 0.286 volt peak to peak @ 75 Ohm available via 4 pin mini connector.

8.   The S-Video input shall have priority over the composite video input.

9.   For loop through connection to external devices there shall be high impedance video outputs foro via 4 pin mini connector.

10.  75  Ohm termination shall be automatically set to OFF when connection is made to the Video high  impedance  monaural audio input available via  an  RCA phono connector.  Audio loop through to external  devices will be available via through an  RCA phono connector.

11.  The monitor shall have a built in 8 Ohm, 0.8 watt speaker for audio monitoring.

D. MECHANICAL REQUIREMENTS

1.   ( SSM-14N1U )

The monitor dimensions shall be 13 5/8"w x 13 3/8"h x 16 5/16"d (346 x 340 x 414mm) and weigh 33           lbs.  (15 kg)

1.   ( SSM-20N1U )

The monitor dimensions shall be 17 11/16"w x 17 3/8"h x 19 3/4"d (449 x 441 x 502mm) and weigh.          61 lbs. 10oz.  (28kg)

2.   Front panel controls shall feature push button On/Off ,  and selection of on screen programming              options.

E. ENVIRONMENTAL REQUIREMENTS

1.   The operating temperature shall be 32 degrees F  to 95 degrees F  (0 degrees C  to +35 degrees C).               Operating humidity shall be 20 percent to 80 percent,  non-condensing.

2.   The monitor will be suitable for indoor applications.  Proper ventilation shall be required to maintain              operating temperature  when mounted in  equipment cabinets or  other confined areas.

F. REFERENCES

1.   UL Listed 1950 - Information Technology Equipment Including Electrical Business Equipment

2.   CSA Listed C22.2 # 950

3.   FCC Verified, Class A Digital Device

G. ACCESSORIES

1.   Optional

a. MB-14N1U - 19" rack mount adaptor for  SSM-14N1U.  Rack kit  height is 8 units ( 14")

b. SLR-103A - Slide Rail Kit for  SSM-20N1U.  Rack height is 10 units ( 17.5")

(1996 Sony Electronics Inc.  All rights reserved.  Feature and specifications subject to change without notice.  Non-metric weights and measurements are approximate.  SONY, Trinitron and Nothing Escapes Us aretrademarks of Sony.