ARCHITECT & ENGINEER SPECIFICATIONS

SECTION 16780

VIDEO SURVEILLANCE SYSTEMS

Model: SSM-14/20N5U

14” & 20” Color Monitor

# PART 2  	PRODUCTS

2.01 	CCTV MONITOR SPECIFICATIONS

## A. 	VIDEO - GENERAL REQUIREMENTS

1.   (SSM-14N5U)

The monitor shall be color, with a 13-inch diagonal viewing area.

1.  (SSM-20N5U)

The monitor shall be color, with a 19-inch diagonal viewing area.

2.   The monitor shall have on screen menu programming.

3.   The monitor shall be capable of workstation surface mounting or EIA standard 19" rack mounting with optional rack mount assembly.

### B. 	VIDEO - ELECTRICAL REQUIREMENTS

1.   The input voltage shall be AC 100 to 240 volts, 50/60 Hz.

2.   (SSM-14N5U)

Power consumption shall be 80 watts maximum.

2.   (SSM-20N5U)

Power consumption shall be 100 watts maximum.

3.   The signal system shall be NTSC/PAL/SECAM/NTSC 4.43.

4.   The horizontal resolution at center shall be 500 lines.

5.   The monitor shall have a color temperature rating of 6500 degrees K.

6.   The monitor shall provide one (1) composite video input.  The input shall be 1.0-volt peak to peak @ 75 Ohms, sync negative via BNC connectors.

7.   There shall be an S-Video (Y/C) input, Y (Luminance) 1.0-volt peak to peak @ 75 Ohm, sync negative, C (Chrominance) 0.286-volt peak to peak @ 75 Ohm available via 4 pin mini connector.

8.   The S-Video input shall have priority over the composite video input.

9. 	For loop through connection to external devices, there shall be high impedance video outputs for composite video via BNC connector, and S-Video via 4 pin mini connector.

- 75-Ohm termination shall be automatically set to OFF when connection is made to the Video Out connector.

C. AUDIO REQUIREMENTS

1.   The monitor shall have a -5 dbs high impedance monaural audio input available via an RCA Phono connector.  Audio loop through to external devices will be available via an RCA Phono connector.

2.   The monitor shall have a built in 8-Ohm, 0.8-watt speaker for audio monitoring.

### D. 	MECHANICAL REQUIREMENTS

1.   (SSM-14N5U)

The monitor dimensions shall be 13 5/8"w x 13 3/8"h x 16 5/16"d (346 x 340 x 414mm) and weigh 33 lb.  (15 kg)

1.   (SSM-20N5U)

The monitor dimensions shall be 17 11/16"w x 17 3/8"h x 19 3/4"d (449 x 441 x 502mm) and weigh 61 lb. 10oz.  (28kg)

2.   Front panel controls shall feature push button On/Off, and selection of on screen programming options.

### E. 	ENVIRONMENTAL REQUIREMENTS

1.   The operating temperature shall be 32 degrees F to 95 degrees F (0 degrees C to +35 degrees C).  Operating humidity shall be 20 percent to 80 percent, non-condensing.

2.   The monitor will be suitable for indoor applications.  Proper ventilation shall be required to maintain operating temperature when mounted in equipment cabinets or other confined areas.

### F. 	REFERENCES

1.   UL Listed 1950 - Information Technology Equipment Including Electrical Business Equipment

2.   CSA Listed C22.2 # 950

3.   FCC Verified, Class A Digital Device

### G. 	ACCESSORIES

1.   Optional

a.	MB-14N1U - 19" rack mount adaptor for SSM-14N5U.  Rack kit height is 8 units (14")

b. 	SLR-103A - Slide Rail Kit for SSM-20N5U.  Rack height is 10 units (17.5")