ARCHITECT & ENGINEER SPECIFICATIONS

SECTION  16780

VIDEO SURVEILLANCE SYSTEMS

SSM-175

17” Monochrome Monitor

PART 2	 PRODUCTS

2.01	CCTV MONITOR SPECIFICATIONS

A. 	VIDEO - GENERAL REQUIREMENTS

1.   The monitor shall be  black and white (monochrome) measuring 17" diagonally.

2.   The monitor shall be capable of work station surface mounting or EIA standard 19" rack 	mounting with optional rack mount assembly.

B. 	VIDEO - ELECTRICAL REQUIREMENTS

1.   The input voltage shall be AC 120  volts, 60 Hz.  Power consumption shall be 35 	watts.

2.   The signal system shall be EIA Monochrome Standard.

3.   The horizontal resolution at center shall be more than 850 lines.

4.   The horizontal linearity shall be <  (10 percent.  The vertical linearity shall be <  (8 	percent.

5.   The brightness at high light setting with all white picture signal shall be 130 nt

(clamp on).

6.   The monitor shall have two  composite video inputs labeled   A & B.  Each input shall be 	0.5 - 2.0  volts peak to peak @ 75 Ohms, sync negative via BNC connectors.  Video input 	viewing will be selectable, A/B,  through push button controls.

7.   The monitor shall have  switch selectable (On/Off)  75 Ohm termination or high 	impedance composite  video loop through available for connection to external devices via 	BNC connector.

8.   The monitor shall have switch selectable (On/Off) DC clamp for stable black level 	reference.

C. 	MECHANICAL REQUIREMENTS

1.   The monitor dimensions shall be 16 3/4"w x 16 1/8"h x 15"d ( 424 x 409 x 380mm) and

weigh 38lbs. 9 oz. (17.5kg)

2.   Front panel controls shall feature push button On/Off, Video Input A/B,  and rotary 	Horizontal Hold,  Vertical Hold,  Brightness and  Contrast controls.

3.   Rear panel controls shall feature slide switch selectable On/Off  75 Ohm termination for 	video inputs  A & B  and DC clamp controls.

D. 	ENVIRONMENTAL REQUIREMENTS

1.   The operating temperature shall be 32 degrees F  to 95 degrees F (0 degrees C to +35 	degrees C).  Operating humidity shall be less than 80 percent,  non-condensing.

2.   The monitor will be suitable for indoor applications.  Proper ventilation shall be required 	to maintain operating temperature  when mounted in  equipment cabinets or  other 	confined areas.

E. 	REFERENCES

1.   UL Listed 1410 - Television Receivers and High Voltage Video Products

2.   CSA Listed C22.2 # 1

3.   FCC Verified, Class A Digital Device

F. 	ACCESSORIES

1.   Optional

a. 	RMM-171- 19" rack mount ears for single SSM-175 configuration.  Rack kit  height is 9 units  (15.75")

(1997 Sony Electronics Inc.  All rights reserved.  Feature and specifications subject to change without notice.  Non-metric weights and measurements are approximate.  SONY and Nothing Escapes Us are trademarks of Sony.