ARCHITECT & ENGINEER SPECIFICATIONS

SECTION  16780

VIDEO SURVEILLANCE SYSTEMS

SSM-8040

8" Color Monitor

PART 	2  PRODUCTS

2.01 	CCTV MONITOR SPECIFICATIONS

A. 	VIDEO - GENERAL REQUIREMENTS

1. 	The monitor shall be color, with viewable screen size of 8", measured diagonally.

2.   The monitor shall be capable of work station surface mounting or EIA standard 19" rack mounting with optional rack mount assembly.

B. 	VIDEO - ELECTRICAL REQUIREMENTS

1.   The input voltage shall be AC 120 volts, 50/60 Hz.  Power consumption shall be 39 watts.

2.   The signal system shall be EIA and the color standard shall be NTSC.

3.   The horizontal resolution at center shall be more than 250 lines.

4.   The horizontal linearity shall be less than 5 percent.  The vertical linearity shall be less than 5 percent.

5.   The monitor shall have a  composite video input, 1.0 volt peak to peak @ 75 Ohms, sync negative via BNC connector.

6. 	Video input shall be 75 Ohm auto terminating, when no external devices are connected to the video output  terminal of the monitor.

C. 	MECHANICAL REQUIREMENTS

1.   The monitor dimensions shall be 8 5/8"w x 8 5/8"h x 14"d ( 217 x 217 x 352.5 mm) and weigh 17 lbs. 3 oz. (7.8 kg)

2.   Front panel controls shall feature push button On/Off  and rotary style knobs for brightness, chroma, phase and contrast.

3.   The rear panel  shall feature a mini rotary button  for vertical hold control.

D. ENVIRONMENTAL REQUIREMENTS

1.   The operating temperature shall be 32 degrees F to  95 degrees F (0 degrees to +35 degrees C).  Operating humidity shall be 20 percent to 80 percent,  non-condensing.

2.   The monitor will be suitable for indoor applications.  Proper ventilation shall be required to maintain operating temperature  when mounted in  equipment cabinets or  other confined areas.

E. 	REFERENCES

1.   UL Listed 1410 - Television Receivers and High Voltage Video Products

2.   CSA Listed C22.2 # 1

3.   FCC, Class A

4.   IC,  Class  A

F. ACCESSORIES

1.   Optional

a. 	MB-507- 19" rack mount adaptor for dual SSM-8040 configuration. Rack kit height is 5 units ( 8.75")

b. 	MB-509 - Blank plate cover for single SSM-8040 configuration installed in MB-507.

(1998 Sony Electronics Inc.  All rights reserved.  Features and specifications are subject to change without notice.  Non-metric weights and measurements are approximate.  SONY, Hyper Had, Trinitron, CCD-Iris and Nothing Escapes Us are trademarks of Sony.