ARCHITECT & ENGINEER SPECIFICATIONS

SECTION  16780

VIDEO SURVEILLANCE SYSTEMS

Model: SSM-930

9” Monochrome Monitor

PART 2  PRODUCTS

2.01 CCTV MONITOR SPECIFICATIONS

A. VIDEO - GENERAL REQUIREMENTS

1.   The monitor shall be  black and white (monochrome) measuring 9" diagonally,  90  deflection.

2.   The monitor shall be capable of work station surface mounting or EIA standard 19" rack mounting              with optional rack mount assembly.

B. VIDEO - ELECTRICAL  REQUIREMENTS

1.   The input voltage shall be AC 120 volts,  60 Hz.  Power consumption shall be 27 watts.

2.   The signal system shall be EIA Monochrome Standard.

3.   The horizontal resolution at center shall be more than 750 lines.

4.   The horizontal linearity shall be <  +11 percent.  The vertical linearity shall be <  +8 percent.

5.   The brightness at high light setting with all white picture signal shall be 250 nt + 50 nt.

6.   The composite video input shall be 1.0 volt   peak to peak @ 75 Ohms, sync negative via BNC              connector.

7.   The monitor shall have  switch selectable (On/Off)  75 Ohm termination or high impedance composite             video loop through available for connection to external devices via BNC connector.

8.   The monitor shall have switch selectable (On/Off) DC clamp for stable black level reference.

C. MECHANICAL  REQUIREMENTS

1.   The monitor dimensions shall be 8 5/8"w x 8 3/4"h x 9 3/4"d ( 219 x 220 x 246mm) and

weigh 13 lbs. (5.8kg)

2.   Front panel controls shall feature push button On/Off and rotary Horizontal Hold,  Vertical Hold,               Brightness and  Contrast controls.

3.   Rear panel controls shall feature On/Off switches for 75 Ohm termination  and DC clamp controls.

D. ENVIRONMENTAL  REQUIREMENTS

1.   The operating temperature shall be 32 degrees F  to 104 degrees F (0 degrees C to +40 degrees C).               Operating humidity shall be 20 percent to 80 percent,  non-condensing.

2.   The monitor will be suitable for indoor applications.  Proper ventilation shall be required to maintain              operating temperature  when mounted in  equipment cabinets or  other confined areas.

E. REFERENCES

1.   UL Listed 1410 - Television Receivers and High Voltage Video Products

2.   CSA Listed C22.2 # 1

3.   FCC Verified Unintentional Radiator,  All Other Devices

F. ACCESSORIES

1.   Optional

a. MB-900 - 19" rack mount adaptor with trim panel for dual SSM-930 configuration.  Rack kit               height is 5 units ( 8.75")

b. BP-900 - Blank panel for MB-900 when one SSM-930 is installed.

(1995 Sony Electronic Inc.  All rights reserved.  Feature and specifications subject to change without notice.  Non-metric weights and measurements are approximate.  SONY and Nothing Escapes Us are trademarks of Sony.