ARCHITECT & ENGINEER SPECIFICATIONS

SECTION  16780

VIDEO SURVEILLANCE SYSTEMS

SVT-124

24 Hour VHS Time Lapse Recorded

PART  2	PRODUCTS

2.01	CCTV TIME LAPSE VIDEO RECORDER SPECIFICATIONS

A.	VIDEO - GENERAL REQUIREMENTS

1.   The VTR (video tape recorder) shall utilize standard VHS tape format.

2.	The recording system shall be Dual Azimuth,  4-Head helical  scanning system.

3.   The VTR shall feature three (3) user programmable time lapse recording modes. The time 	modes 	shall be 2/12/24 hour

4.   The VTR shall feature a menu driven, on screen display for programming system 	functions 	and 	unit status.  This shall be possible with or without an active video input.

5.   There shall be a programmable, position selectable,  time/date generator which shall 	display month, 	day, year, hour, minute and second in a shadow character format.

6.   For unattended continuous recording the VTR shall feature an automatic repeat record 	setting.  	This function shall be automatically overridden in the event of an alarm.

7.   The VTR shall be capable of video signal loop through on power off mode, and E-E 	mode 	during 	normal power ON conditions.

8.   The VTR shall provide a dry contact input terminal to allow recording start and stop via 	external 	equipment or timers.

9.   The VTR shall have provisions to allow entry of up to 20 days, designated as non 	working 	days 	which shall follow the holiday record setting on the timer program.

10. The VTR shall provide a  record check function that when activated shall rewind the tape 	for 	approximately three (3) seconds and playback the tape for approximately two (2)  	seconds.  The unit 	shall then return to its original record mode.

11. The VTR shall provide a  mini jack for connection of an external remote control device.

12. The VTR shall feature automatic head cleaning.

13. To protect against unauthorized use or accidental system changes the VTR  shall feature a 	programmable security lock feature.

14. The VTR shall provide a Used Time indicator which shall show used time on the drum 	head and 	the power on time on the monitor.

B.	 VIDEO - ELECTRICAL REQUIREMENTS

1.   The input voltage shall be AC 120 volts, 60 Hz.  Power consumption shall be 17 watts.

2.   The VTR shall have thirty (30) day power protection failure for time/date and record 	mode.

3.   The signal system shall be EIA / NTSC standard for color video signals.

4.  The VTR shall produce a minimum 350 horizontal lines resolution , monochrome and 300 	horizontal lines resolution, color.

5.  To obtain optimum picture performance the VTR shall feature Adaptive Picture Control 	(APC)  	which automatically adjusts for the optimum video head bias based on the current 	condition of the 	tape and the video heads.

6.   The composite video input shall be 1.0 volt  peak to peak @ 75 Ohms, unbalanced via 	BNC 	connector.

7.   The VTR shall be capable of video signal loop through on power off mode, and E-E 	mode 	during 	normal power ON conditions..

8.   The composite video output shall be 1.0 volt  peak to peak @ 75 Ohms,  unbalanced via 	BNC 	connector.

9.   The signal to noise ratio shall be more than 44 dB (SP).

10.  The approximate recording intervals for each record mode, with T-120 tape, shall be - 2 	hr/1/60 	sec; 12 hr/0.12 sec; 24 hr/0.22 sec.

11.  A +5V, 5.7 kOhm (active low) switch pulse output terminal shall be provided for 	interfacing with 	externally driven switchers, multiplexers or other devices.  Switch pulse 	output of the unit shall be 	field or frame selectable.  It shall be selectable for 	1,2,3,4,5,10,30  or 60 frames(s)/field(s).

12. The recorder shall feature stationary erase head configuration.

13. The fast forward/ rewind time with a T-120 tape shall be approximately 2.5 minutes.

C.  AUDIO REQUIREMENTS

1.   Audio recording shall be available in the 2, 12, and 24 hour recording modes.

2.   The audio input  shall be -7.8 dBs @ 47 kOhms via an Phono style connector.

3.   The audio output shall be -7.8 dBs  @ 600 Ohms via an Phono style connector.

4.   The VTR shall provide a MIC input , -60 dBs, 600 Ohm via a mini jack connector.

D.   ALARM REQUIREMENTS

1.   For alarm record mode activation from external devices the VTR shall provide a normally 	open, 	dry contact input via screw terminals.

2.   There shall be a +5  volts,  4.7 kOhms alarm output available via screw terminals for 	connection to 	external devices.  The alarm output shall follow alarm input activation, 	active 	low.

3.   The alarm recording speed shall be preset in the 2 hour mode.

4.   The VTR shall be fitted with a built-in buzzer which shall be activated during alarm 	recording or 	end of tape.  This buzzer shall be capable of being manually 	activated/deactivated.

5.   The VTR shall have switch selectable alarm duration speeds of twenty (20) seconds, one 	(1) minute, 	or follow the alarm activation period.

6.   An on-screen alarm recall log shall display the last eight (8) alarms by alarm count, 	month,  day 	and time of occurrence, plus a running count of up to 999 alarm activations.

7.   To audit and select alarm activation's for viewing, the VTR shall have the Alarm Scan 	feature. 	Activating the alarm scan feature shall bring the VTR into FF mode, play/pause 	the 	first five 	seconds of each alarmed segment on the tape.

8.   A warning out signal shall be provided in the event recording is interrupted due to tape 	jam.

9 .   For signaling the end of the video tape a screw terminal output, +5 volts, 4.7 kOhm 	signal 	shall 		be provided, active low.  The alarm buzzer shall also activate. Additionally, 	this terminal 	shall 	be selectable to issue “tape before end out” pulses when the counter 	reads 01H57M00S (T120)

E.   MECHANICAL REQUIREMENTS

1.   For  rack mount accessibility  the VTR shall feature front panel tape loading.

2.   The recorder  dimensions shall be 9 1/2"w x 3 7/8"h x 13 1/8"d  ( 240 x 96.5 x 333 mm ) 	and weigh 	8 lb.  6 oz.   (3.8 kg)

3.   The VTR  shall be capable of work station surface or shelf mounting.

F.   ENVIRONMENTAL REQUIREMENTS

1.  The operating temperature shall be 41 degrees F  to 104 degrees F  (5 degrees C to +40 	degrees C).  Operating humidity shall be 80 percent or less,  non-condensing.

2.   The recorder will be suitable for indoor applications.  Proper ventilation and filtering 	shall 	be 	required to maintain operating temperature and air quality  when mounted in  	equipment 	cabinets or  	other confined areas.

G.   REFERENCES

1.   UL Listed 1409 - Low-Voltage Video Products Without Cathode-Ray-Tube Displays

2.   CSA Listed C22.2 # 1

3.   FCC Verified, Class A Digital Device

H.   ACCESSORIES

1.   Optional

a. 	T-120PM - 120 minute VHS Tape

b.	SVT-RM10 Remote Control Unit

(1997 Sony Electronics Inc.  All rights reserved.  Features and specifications subject to change without notice.  Non-metric weights and measurements are approximate. SONY and Nothing Escapes Us are trademarks of Sony.