ARCHITECT & ENGINEER SPECIFICATIONS

SECTION  16780

VIDEO SURVEILLANCE SYSTEMS

SVT-S3100

168 Hour -S-VHS Time Lapse Recorder

PART 2  PRODUCTS

2.01 CCTV TIME LAPSE VIDEO RECORDER SPECIFICATIONS

A. VIDEO - GENERAL REQUIREMENTS

1.   The VTR (video tape recorder) shall utilize standard VHS and S-VHS tape format.  Tape format shall              be automatically selected based on the tape format used.

2.   The recording system shall be rotary two-head helical scanning.

3.   The VTR shall feature on screen programming for  set up of system functions.

4.   The VTR shall feature seven (7) user programmable time lapse recording modes. The time modes shall              be 2/12/24/48/72/96/120/168 hour with a T-120 tape.

5.   The VTR shall feature Automatic Picture Control (APC), which automatically adjusts for the optimum              video head bias based on the current condition of the tape and the video heads.

6.   There shall be a programmable, position selectable,  time/date generator which shall display month, day,              year/hour, minute and second in a shadow character format.

7.   A +5  volts,  5.7k Ohm switch output for video record timing will be provided via screw terminals for              connection to external devices.

8.   The VTR shall provide a  mini jack for connection of an external remote control device.

9.   For unattended continuous recording the VTR shall feature a programmable repeat record setting.

10.  To allow for automatic program changes the recorder shall feature  seven (7) day,  seven (7) event, plus              Daily event internal timer capabilities.  For connection to external devices there shall be a +12  volts,              5.7k Ohm  terminal output that follows timer activations.

11.  The VTR shall provide an exception schedule that allows for twenty (20) non-working days  or holidays              to have specific start/stop times.

12.  The VTR shall feature on screen viewing of operating parameters.

13.  The recorder shall feature automatic head cleaning.

14.  To protect against unauthorized use or accidental system changes the VTR  shall feature a              programmable security lock feature.

B. VIDEO - ELECTRICAL REQUIREMENTS

1.   The input voltage shall be AC 120 volts, 50/60 Hz.  Power consumption shall be 22 watts.

2.   The VTR shall have thirty (30) day power protection failure for time/date and selected mode.

3.   The signal system shall be EIA / NTSC standard for color video signals.

4.   In the S-VHS mode the VTR shall produce a minimum of 430 horizontal lines resolution, monochrome,              and 400 horizontal lines, color.

5.   In VHS mode the VTR shall produce a minimum 300 horizontal lines resolution , monochrome and 240              horizontal lines resolution, color.

6.   There shall be one (1) composite video input, 1.0 volt  peak to peak @ 75 Ohms, unbalanced via BNC              connector.  This output shall be looping even when power to the unit is turned off.

7.   There shall be an  S-Video (Y/C) input, Y (Luminance) 1.0 volt peak to peak @ 75 Ohm, sync negative,              C (Chrominance) 0.286 volt peak to peak @ 75 Ohm available via 4 pin mini connector.

8.   The composite video output shall be 1.0 volt  peak to peak @ 75 Ohms,  unbalanced via BNC              connector.

9.   There shall be an S-Video (Y/C) output, Y (Luminance) 1.0 volt peak to peak @ 75 Ohm, sync              negative, C (Chrominance) 0.286 volt peak to peak @ 75 Ohm available via 4 pin mini connector.

10.  The signal to noise ratio shall be more than 45 dB (S-VHS).

11.  The approximate recording intervals for each record mode, with T-120 tape, shall be - 2 hr/1/60 sec;              12 hr/0.1 sec; 24 hr/0.2 sec; 48 hr/0.4 sec; 72 hr/0.6 sec; 96 hr/0.8 sec; 120 hr/1.0 sec; 168 hr/1.4 sec.

12.  The recorder shall feature stationary erase head configuration.

13.  The VTR shall provide manual controls for NORMAL and SLOW tracking adjustments.

14.  The fast forward/ rewind time with a T-120 tape shall be less than  four (4) minutes.

C. AUDIO REQUIREMENTS

1.   Audio recording shall be available in the 2, 12, and 24 hour recording modes.

2.   The audio input  shall be -7.8dBu @ 100k Ohms via an Phono style connector.

3.   The audio output shall be -7.8dBu @ 600k Ohms via an Phono style connector.

4.   The VTR shall provide a MIC input , -60dBu, high impedance via a mini jack connector.

D. ALARM REQUIREMENTS

1.   For alarm record mode activation from external devices the VTR shall provide a normally open dry              contact input via screw terminals.

2.   There shall be a +5  volts @ 5.7k Ohms alarm output available via screw terminals for connection to              external devices.  The alarm output shall follow alarm input activation, active low.

3.   The alarm recording speed shall be programmable 2 hour/12 hour or No Change (time lapse mode)

4.   The alarm record duration shall be programmable for 20 seconds, 1 minute, or "CC" mode, which stays              in the alarm mode as long as the alarm input remains active.

5.   To audit and select alarm activations for viewing,  the first five seconds of each alarm activation may              be viewed via the alarm scan feature.

6.   An on screen alarm log shall list the last eight alarm activations by alarm count  number (up to 999)               month, date and time of day.

7.   For signaling the end of the video tape screw terminal outputs, +5  volts @ 5.7k Ohm trigger signal              shall be provided, active low.

E. MECHANICAL REQUIREMENTS

1.   For  rack mount accessibility  the VTR shall feature front panel tape loading.

2.   The recorder dimensions shall be 16 5/8"w x 4"h x 13 1/2"d  ( 420 x 100 x 340mm ) and weigh 12 lb.               13 oz.   (5.8 kg)

3.   The VTR  shall be capable of work station surface mounting or EIA standard 19" rack mounting with              optional rack mount assembly.

F.  ENVIRONMENTAL REQUIREMENTS

1.   The operating temperature shall be 41O F  to 104O F  (5O c to +40OC).  Operating humidity shall be less than 80 percent,  non-condensing.

2.   The recorder will be suitable for indoor applications.  Proper ventilation and filtering shall be required              to maintain operating temperature and air quality  when mounted in  equipment cabinets or  other              confined areas.

G. REFERENCES

1.   UL Listed 1409 - Low-Voltage Video Products Without Cathode-Ray-Tube Displays

2.   CSA Listed C22.2 # 1

3.   FCC Verified, Class A Digital Device

H. ACCESSORIES

1.   Optional

a. SMB-5000 Rack Mount Kit - 3 units high (5.25")

b. SVT-RS100 - RS-232C interface board.

( 1996 Sony Electronic Inc.  All rights reserved.  Feature and specifications subject to change without notice.  Non-metric weights and measurements are approximate. SONY, Remote Commander, WatchCorder, Hi8, Rotary Flying Erase and Nothing Escapes Us are trademarks of Sony.