ARCHITECT & ENGINEER SPECIFICATIONS

SECTION  16780

VIDEO SURVEILLANCE SYSTEMS

UP-2100SD

Color Video Printer

PART 	2 	PRODUCTS

2.01 	CCTV  PRINTER SPECIFICATIONS

A.	 VIDEO - GENERAL REQUIREMENTS

1. 	The printing method shall utilize Dye Transfer Sublimation Process.

2.  	The printer head resolution shall be 150 dots per inch.

3. 	The maximum print size shall be 80 x 100 mm.

4. 	The maximum effective dot resolution shall be 720h x 468v, full size print.  The printer system utilize 256 level  process producing over 16.7 million colors per dot.

5. 	Picture memory shall be one frame, (8 bits x RGB three color process) The printer shall provide split memory  capabilities to allow the saving of one (1), two (2), four (4) or sixteen (16) pictures to memory.  Stored pictures may  be viewed on the viewing monitor.

6. 	The printer shall allow for color adjustments of live pictures.

7. 	Printer shall provide internal character generation for print caption.

a.	Print caption forty eight (48) characters, outside of the print  area.

8. 	Print time shall be within 75 seconds.

9. 	Printer shall have wired/wireless remote print capabilities shall via optional RM-5500/1 remote controller.

B.   VIDEO - ELECTRICAL REQUIREMENTS

1. 	The input voltage shall be ac 120 volts, 50 / 60 Hz.  Power consumption shall be 1.5 amps.  Power cord  shall be three prong grounded type.

2. 	The printer shall accept EIA/NTSC signal scanning system/color standards.

3. 	Selection of incoming video, Y/C or Composite, shall be menu controlled.

4. 	Composite and Y/C video inputs shall automatically loop through to the outputs at the absence of AC power, or the power switch is turned off.

5. 	Looping of input video shall only be to a terminated monitor.

6. 	There shall be no more than one monitor hooked up to the video printer.

C.   MECHANICAL REQUIREMENTS

1. 	The printer dimensions shall be 14 13/16"h x 4 15/16"w x 16 1/4"d (370 x 125 x 413 mm) and weigh 18 lb. 12 oz.  (9 kg)

2.  	Print media supply tray shall be 200 sheets.

3.  	Each box of media (UP-2010) shall contain a ribbon cassette, and 4 individually sealed packs of fifty sheets of the receiver (print paper).

4.  	Print media (Ribbon & receiver), including finished  prints shall be accessible via the front of the unit.

5.  	A removable panel shall be provided on the top of the unit, which shall be positioned over the print roller assembly, to allow removal of jammed media.

6.  	Menu, cursor and programming buttons shall be accessible from the front of the unit.  These buttons shall be located behind the front lid, which shall also serve as access for the ribbon cassette.

D.   ENVIRONMENTAL REQUIREMENTS

1. 	The operating temperature shall be 32 degrees F to 104 degrees F (0 degrees C to +40 degrees C).  Operating  humidity shall be 20 percent to 80 percent,  non-condensing.

2. 	The printer will be suitable for indoor applications.  Proper ventilation shall be required to maintain operating  temperature  when mounted in  equipment cabinets or  other confined areas.

E.   REFERENCES

1. 	UL Listed 1950 - Information Technology Equipment Including Electrical Business Equipment

2. 	CSA C2.22 No. 950

3. 	FCC , Class A

4. 	IC, Class A

F.   ACCESSORIES

1. 	Supplied

a.   Operating Manual x 1

b.   Paper Tray            x 1

c.   Print Tray              x 1

d.   AC Power Cable.

2. 	Optional

a.   RM-5500/1  Wired/wireless remote controller

b.  UPC-2010 Color Print Pack

(1998 Sony Electronics Inc.  All rights reserved.  Features and specifications are subject to change without notice.  Non-metric weights and measurements are approximate.  SONY, Hyper Had, Trinitron, CCD-Iris and Nothing Escapes Us are trademarks of Sony.