ARCHITECT & ENGINEER SPECIFICATIONS

SECTION  16780

VIDEO SURVEILLANCE SYSTEMS

Model: UP-880

Monochrome Video Printer

PART 2  PRODUCTS

2.01 CCTV PRINTER SPECIFICATIONS

A. VIDEO - GENERAL REQUIREMENTS

1.   The printing method shall be thermal head utilizing a 1024 dot drive system which shall produce a print              with a resolution of 10.2 dots per millimeter (259 dpi).

2.   The printer shall provide two print modes. Standard print mode, aspect ratio 4:3, and Side print mode,              aspect ratio 3:4.  Print modes shall be selectable via a front panel slide switch.

3.   Each print  mode shall have five (5)  user selectable print options of Normal Mode, Small Mode,  1.5X              Zoom Mode, 2.0X Zoom Mode, and Large Mode. Print option modes shall be selectable via front panel              rotary  switch.

4.  The available scan modes shall correspond to the selected print sizes of  Normal, Wide 1, Wide 2.  Scan              modes shall be rear panel dip switch selectable.

5.   Effective pixel resolution  shall vary depending on the print size and scanning system selected.  Refer              to Appendix 1 for pixel and resolution specifications.

6.   The printer system shall process 256 gray levels.

7.   Picture  memory shall be dip switch selectable for frame or field.

8.   Picture  memory shall be 1024 x 768 x 6 bits.

9.   The printer shall produce finished video prints in approximately four (4) seconds in the Standard Print              Mode and approximately seven (7) seconds in the Side Print  Mode.

B. VIDEO - ELECTRICAL REQUIREMENTS

1.   The input voltage shall be ac 120 volts, 50 / 60 Hz.  Power consumption shall be 1.8 amps.

2.   The composite video input shall be 1.0 volt peak to peak @ 75 Ohms, sync negative via BNC connector.

3.   The composite video input shall be dip switch selectable (On/Off), loop through 1.0 volt peak to peak              @ 75 Ohms,  sync negative via BNC connector.

4.   The printer shall feature automatic selection of  either EIA (525 Lines) or CCIR (625 Lines) system              standards.

5.   Aspect ratio shall be dip switch selectable for 4:3 or 1:1.

6.   The printer shall have front panel selection for EE mode to adjust contrast and brightness before              printing.

C. MECHANICAL REQUIREMENTS

1.   The printer dimensions shall be 6"h x 4 3/16"w x 11 15/16"d (154 x 106 x 303mm) and

weigh 8 lbs. 2 oz. (3.7kg)

2.   The printer shall use standard or high density thermosensitive paper and provide approximately  230              prints per roll ( w/ UPP-110HA).

3.   Wired remote control capabilities shall be available via stereo mini jack.

D. ENVIRONMENTAL REQUIREMENTS

1.   The operating temperature shall be 32 degrees F to 104 degrees F (0 degrees C to +40 degrees C).               Operating humidity shall be 20 percent to 80 percent,  non-condensing.

2.   The printer will be suitable for indoor applications.  Proper ventilation shall be required to maintain              operating temperature  when mounted in  equipment cabinets or  other confined areas.

E. REFERENCES

1.   UL Listed 1950 - Information Technology Equipment Including Electrical Business Equipment

2.   CSA Listed C 22.2 # 950

3.   FCC Verified, Class A Digital Device

F. ACCESSORIES

1.   Supplied

a. AC Power Cord

b. UPP-110HA High Density Paper Roll

c. BNC to BNC Video Cable

d. Head Cleaning Sheet.

2.   Optional

a. RM-91 Wired Remote Commander

b. FS-20 Wired Foot Switch.

c. UPP-110S/3 - Standard Paper

d. UPP-110HD - High Density Paper

e. UPP-110HA - Wide Dynamic Range Paper

(1995 Sony Electronics  Inc. All rights reserved.  Features and specifications subject to change without notice.  Non-metric weights and measurements are approximate. SONY,  Remote Commander, and Nothing Escapes Us are trademarks of  Sony.