ARCHITECT & ENGINEER SPECIFICATIONS

SECTION  16780

VIDEO SURVEILLANCE SYSTEMS

Model: UP-910

Monochrome Video Printer

PART 2  PRODUCTS

2.01 CCTV PRINTER SPECIFICATIONS

A. VIDEO - GENERAL  REQUIREMENTS

1.   The printing method shall be thermal head utilizing a 768 dot drive system.

2.   The print size, with an aspect ratio of 4:3,  shall be selectable via dip switch settings for  Normal, Wide              1 and Wide 2.  The print size shall meet the following criteria: Print Size - EIA  Inches/Millimeters

Normal: 7 1/4" x 5 5/8" / 182 x 140 mm

Wide 1: 7 5/8" x 5 3/4"  / 192 x 146 mm

Wide 2: 7 7/8" x 6" / 200 x 150 mm

3. Effective pixel resolution  shall vary depending on the print size and scanning system selected.  The  vailable scan modes shall correspond to the selected print sizes of Normal, Wide 1, Wide 2. The pixel resolution  will meet the following criteria: Mode/Size EIA

Normal: 700 Dots x 472 Lines

Wide 1: 736 Dots x 490 Lines

Wide 2 : 768 Dots x 508 Lines

4.   The printer system shall process 128 gray levels.

5.   Picture memory shall be dip switch selectable for frame or field.

6.   The printer shall produce finished video prints in approximately 20 seconds per captured screen.

7.   Wired remote control capabilities shall be available via stereo mini jack.

B. VIDEO - ELECTRICAL  REQUIREMENTS

1.   The input voltage shall be ac 120 volts, 50 / 60 Hz.  Power consumption shall be 2.5 amps.

2.   The composite video input shall be 1.0 volt  peak to peak @ 75 Ohms, sync negative via BNC  connector.

3.   The composite video output shall be switch selectable loop (On/Off) through 1.0 volt  peak to peak @ 75 Ohms, sync negative via BNC connector.

4.   The printer shall feature automatic selection of  either EIA (525 Lines) or CCIR (625 Lines) system  standards.

5.   Aspect ratio shall be dip switch selectable for 4:3 or 1:1.

C. MECHANICAL  REQUIREMENTS

1.   The printer dimensions shall be 16 3/4"w x 5 1/8"h x 15"d (424 x 130 x 380mm) and

weigh 20 lbs. 1 oz. (9.1kg)

2.   The printer shall use standard or high density thermosensitive paper and provide approximately 130  prints per roll.

D.   ENVIRONMENTAL REQUIREMENTS

1. The operating temperature shall be 32 degrees F to 104 degrees F (0 degrees C to +40 degrees C).   Operating humidity shall be 20 percent to 80 percent,  non-condensing.

2. The printer will be suitable for indoor applications.  Proper ventilation shall be required to maintain operating temperature  when mounted in  equipment cabinets or  other confined areas.

E.   REFERENCES

1. UL Listed 544 - Medical and Dental Equipment

2. CSA Listed C 22.2 # 220 & 125

3. FCC Verified, Class A Digital Device

F.   ACCESSORIES

1. Supplied

a.   AC Power Cord

b.   UPP-216HD High Density Paper Roll

c.   BNC to BNC Video Cable

d.   Head Cleaning Sheet

2. Optional

a.   RM-91 Wired Remote Commander

b.   FS-20 Wire Foot Switch.

c.   UPP-216SE Normal Density Paper

d.   UPP-216HD High Density Paper

(1995 Sony Electronics Inc.  All rights reserved.  Feature and specifications subject to change without notice.  Non-metric weights and measurements are approximate. SONY, Remote Commander and Nothing  Escapes Us are trademarks of Sony.