| Feature/Spec | Sony HSR-X200 | Toshiba KVHD-01A |
| --- | --- | --- |
| Refresh rate | Up to 60 pps | Up to 60 pps |
| Record quality levels | Hyper, Super, High, Mid, Low | 3 only – High, Standard, Basic |
| Audio Recording | Yes, up to 0.10 sec refresh only | No |
| Record Refresh rates | 27 settings | 10 settings |
| Pre-reverse play position | User settable | Fixed |
| Digital zoom | Yes, 2X | No |
| Cue/Review | 2,4,8,16X cue 2,4,8X review | 2,4,8,16,30X cue/review |
| HDD capacity | 80GB built-in , 1 additional option | 80GB built-in, 2 additional HDD option, 1 removeable |
| Download options | Memory stick, compact flash, Microdrive, DDS | FDD built-in, removeable HDD |
| Network | Optional 10/100 base T PCMCIA card | 10baseT included |
| Web server | Built-in | Special viewer software included |
| Series recording | Yes | No |
| Password | 3 levels | 1 level |
| Control ports | RS-232C/RS-485 | RS-232C |
| HDD disk mirroring | Yes | No |
| Separate Alarm partition | Yes | No |
| Search | Alarm, Alarm thumbnail, time/date, archive area & Activity detection search | Full list, alarm list, and time/date |
| Thumbnail preview | Yes | No |
| Alarm Recording | 4 modes Mode 1 – always accept alarm Mode 2 – Accept alarm only during timer record Mode 3 – Accept alarm only outside of timer set Mode 4 – Accept alarm w/in timer set, unit not recording | 1 mode |
| Built in Activity detection | Yes | No |
| Post Activity Search | Yes | No |
| Built-in multiplexer decode | Yes, Sony Sanyo Robot DM | No |
| Digital zoom | Yes, 2X | No |