Sony Camera Selection Guide

Sony’s DXC-327B and DXC-D35 dockable Cameras utilize a flexible design that allows for both ENG/EFP and Studio Application usage. As a result, there are many different configuration choices and options available for these products. The purpose of this document is to help you understand which accessories will and will not work with these camera models.

# DXC-327B Camera

DXC-327B Camera Models:

DXC327BH		DXC-327B dockable Lightweight Camera Head Only

DXC327BLPAC	Includes DXC-327BL dockable Lightweight Camera Head, DXF-601 Viewfinder, and VCT-U14 Tripod Adapter

## DXC-327B Camcorder Back:

### Beta SP	PVV-3 The PVV-3 is a Betacam SP dockable recorder unit with color playback capability through VA-300 adapter. Connects directly to DXC-637, DXC-537A and DXC-327A. Comes standard with NiCad Battery mount (NP-1B)

DVCAM	DSR-1/1 The DSR-1/1 is the direct replacement for DSR-1 The only difference from the DSR-1 is that the new model directly accepts the BP-L series Lithium Ion batteries. To utilize NP-1 style batteries, the DC-L1 adapter is required. The DSR-1/1 is small, lightweight and has low power consumption. It docks to both DXC digital and analog color cameras without any adapters. It utilizes a dual cassette mechanism and has a built-in time code generator/reader. It can record up to 3 hours and will also playback consumer DV recorded tape. It also has a record review function, back space editing, full color playback, built-in external microphone power supply, and DC output for wireless microphone. It features ClipLink operation*, camera set-up data file system*, Setup Navi function*, Freeze mix function*, and built-in self-diagnostics*.  Note: *these functions are only available in combination with DXC-D30/D35 series Cameras.

## Lens:	½” Bayonet Mount Lens, (Canon YH or Fujinon S or Sony VCL series Lenses)

## ENG Viewfinder		DXF-601 Quick start 1.5” monochrome viewfinder

## Batteries:

NiCad			NP-1B NiCad battery

BP-90A NiCad battery

Lithium Ion		BP-L40, BP-L60A or BP-L90A battery

NiMh			BP-M50 or BP-M100 battery

Battery Adaptors/ Plates:

BKW-L601 Lithium-ion battery mounting plate for the DSR-1, CA-537/1 and PVV-3. The BKW-L601 replaces the supplied NP-1 battery box and allows the use of  BP-L and BP-M series batteries.

DC-L1	 Battery case for Digital 1000 Camcorder.  Battery case for NP-1B battery for use with the DVW-700/700WS, DNW Camcorders or BVW-D600 when the BKW-L601 is installed.

DC-L90 Battery case for BP-90A battery for use with the DVW-700/700WS, DNW Camcorders or BVW-D600 when the BKW-L601 is installed.

## Chargers/ A/C Adaptors:

NiCad			BC-1WD (four battery charger with “Auto Refresh”)

### BC-410 (four battery charger with “Auto Refresh”, will also charge four BP-90A’s)

Lithium Ion		BC-L120 (four battery charger/ A/C Adaptor)

Lithium Ion/NiMh	BC-M50 (two battery charger)

A/C Adaptors:

AC-550

The AC-550 Power Supply is designed to power all portable acquisition equipment via a 4-pin XLR connector.  The DC Output is 13.5 VDC at 7A.  Input voltage is 100/120/220240 VAC 50-60Hz

CMA-8A

The CMA-8A is an AC adaptor for DXC Series Cameras.

AC-DN2BPAC

The AC-DN2B is both a power supply and battery charger with high current capacity.  The AC-DN2B can operate both sides of a DNW-A220/A225  by using the Aux. output and cable while charging a BP-L60A/90A battery. The maximum current specification is 9 Amperes. The Package includes ACDN2B, AC6CORD & AC15CORD. ***The AC-DN2B will not charge the BP-M series of Nickel Metal Hydride Batteries***

Cases:

Hard			LC-424CP Grey Roller Case from California Plastics.

LC-424TH Grey Roller case from Thermodyne.

Soft	LC-300SZ

Soft carrying bag with shoulders strap and pockets.

## DXC-327B Studio Configurations:

Studio Packages:

DXC327BSTPAC1	Includes DXC-327BH Dockable Lightweight Camera Head, CA-537/1 Camera Adapter, CCU-M5A CCU, DXF-41 4” Viewfinder, and VCT-U14 Tripod Adapter

DXC327BSTPAC2	Includes DXC-327BH Dockable Lightweight Camera Head, CA-537/1 Camera Adapter, CCU-M5A CCU, DXF-51 5” Viewfinder, and VCT-U14 Tripod Adapter

## Camera Control Unit

(CCU):			CCU-M5A

The new CCU-M5A has been introduced as a replacement/improvement of the very popular CCU-M5. The new CCU has been improved to allow longer cable lengths (300m), audio from the camera and teleprompter functions when attached to the new CA-537/1 adapter, yet maintaining its very attractive price point and reliability. Note: the 14-pin output connector available on CCU-M5 is no longer available on CCU-M5A. If a 14-pin connector is required, the Sony Service center can install it at an additional cost.

Camera Adaptor:

Component	CA-537/1

The CA-537/1 has been introduced as a replacement of CA-537, and allows a teleprompter output from the Genlock connector. Use with the CCU-M5A and 26-pin Multi-core cable (CCZ-AXX)

Composite or Y/C	CA-327 w/CCU-M5A and 14-pin Multi-core cable (CCQ-	 				XXAM) *Note: CCU-M5A Modification is Required*

CCU Remote Control:

RMM-7G Miniature remote control for DXC-327, DXC-D30 series, and CCU-M5A. Controls all basic functions.   Optional cables (CCA-7/XX) extend operation to 50 meters.

Studio Viewfinder:

DXF-41 4” B&W Studio Viewfinder (4:3 only)

DXF-51 5” B&W Studio Viewfinder

(4:3/16:9 Switchable)

## Muilticore Cable:

26-Pin			CCZ-A10US 10 meter cable 26-pin male to 26-pin female

(used with CA-537/1)		(33').

CCZ-A25US 25 meter cable 26-pin male to 26-pin female

(82’).

### CCZ-A50US 50 meter cable 26-pin male to 26-pin female

(164’).

CCZ-A100US 100 meter cable 26-pin male to 26-pin

female (333’).

14-Pin			CCQ-10AM 10 meter cable 14-pin male to 14-pin female

(used with CA-327)		(33').

CCQ-25AMUS 25 meter cable 14-pin male to 14-pin					female (82’).

CCZ-50AMUS 50 meter cable 14-pin male to 14-pin

female (164’).

CCZ-100AMUS 100 meter cable 14-pin male to 14-pin

female (333’).

## Cable Accessories

26-Pin Bulk Head

Connector	CCZZ-1B Bulk head connector for CCZ-A cables.

26-Pin In Line

Extension	CCZZ-1E In-line connector for CCZ-A cables.

Notes:

# DXC-D35/D35WS Camera

DXC-D35/D35WS Camera Models:

DXCD35H		DXC-D35 dockable DSP Camera Head Only

### DXCD35L	Includes DXC-D35H dockable DSP Camera Head, DXF-801 Viewfinder, VCT-U14 Tripod Adapter and RM-LG1 Remote Control Unit.

DXCD35WSL	Includes DXC-D35WS dockable DSP 16:9/4:3 Switchable Camera Head, DXF-801 Viewfinder, VCT-U14 Tripod Adapter, and RM-LG1 Remote Control Unit.

DXC-D35/D35WS Camcorder Models:

DSR135LPAC	Includes DXC-D35L Camera, DSR-1/1 dockable Digital VTR, CACH-101 Unified Handle.

PVWD35LPAC	Includes DXC-D35L Camera, PVV-3 dockable Beta SP VTR, CACH-102 Unified Handle.

DSR135WSLPAC	Includes DXC-D35WSL 16:9/4:3 Switchable Camera, DSR-1/1 dockable Digital VTR, CACH-101 Unified Handle.

PVWD35WSLPAC	Includes DXC-D35WSL 16:9/4:3 Switchable Camera, PVV-3 dockable Beta SP VTR, CACH-102 Unified Handle.

## DXC-D35/D35WS Camcorder Back:

### Beta SP	PVV-3 The PVV-3 is a Betacam SP dockable recorder unit with color playback capability through VA-300 adapter. Connects directly to DXC-637, DXC-537A and DXC-327A. Comes standard with NiCad Battery mount (NP-1B)

DVCAM	DSR-1/1 The DSR-1/1 is the direct replacement for DSR-1 The only difference from the DSR-1 is that the new model directly accepts the BP-L series Lithium Ion batteries. To utilize NP-1 style batteries the DC-L1 adapter is required. The DSR-1/1 is small, lightweight and has low power consumption. It docks to both DXC digital and analog color cameras without any adapters. It utilizes a dual cassette mechanism and has a built-in time code generator/reader. It can record up to 3 hours and will also playback consumer DV recorded tape. It also has a record review function, back space editing, full color playback, built-in external microphone power supply, and DC output for wireless microphone. It features ClipLink operation*, camera set-up data file system*, Setup Navi function*, Freeze mix function*, and built-in self-diagnostics*.  Note: *these functions are only available in combination with DXC-D30/D35 series Cameras.

## Lens:	2/3” Bayonet Mount Lens, (Canon J, YJ or Fujinon A series Lenses)

ENG Viewfinder:	DXF-801 Advanced Quick start 1.5" monochrome electronic viewfinder with tri-level tally, display on/off switch, dual level lens lamp, and switchable 16:9/4:3 aspect ratio.

Unified Handles:

Beta SP	CACH-102 Unified handle for use with DXC-D30 series cameras docked to PVV-3 Betacam SP VTR.

DVCAM	CACH-101 Unified handle for use with DXC-D30 series cameras docked to DSR-1/1 DVCAM VTR.

## Batteries:

NiCad			NP-1B

Lithium Ion		BP-L40, 60A or 90A battery

NiMh			BP-M50 or BP-M100 battery

Battery Adaptors/ Plates:

BKW-L601 Lithium-ion battery mounting plate for the DSR-1, CA-537/1 and PVV-3. The BKW-L601 replaces the supplied NP-1 battery box and allows the use of  BP-L and BP-M series batteries.

DC-L1	 Battery case for Digital 1000 Camcorder.  Battery case for NP-1B battery for use with the DVW-700/700WS, DNW Camcorders or BVW-D600 when the BKW-L601 is installed.

DC-L90 Battery case for BP-90A battery for use with the DVW-700/700WS, DNW Camcorders or BVW-D600 when the BKW-L601 is installed.

## Chargers/ A/C Adaptors:

NiCad			BC-1WD (four battery charger with “Auto Refresh”)

BC-410 (four battery charger with “Auto Refresh”, also

will charge four BP-90A’s)

Lithium Ion		BC-L120 (four Battery charger/ A/C Adaptor)

Lithium Ion or NiMh BC-M50 (two battery charger)

A/C Adaptors:

AC-550

The AC-550 Power Supply is designed to power all portable acquisition equipment via a 4-pin XLR Connector.  The DC Output is 13.5 VDC at 7A.  Input voltage is 100/120/220240 VAC 50-60Hz.

CMA-8A

The CMA 8A is an AC adapter for DXC Series Cameras.

A/C Adaptors (cont):

AC-DN2BPAC

The AC-DN2B is both a power supply and battery charger with high current capacity.  The AC-DN2B can operate both sides of a DNW-A220/A225  by using the Aux. output and cable while charging a BP-L60A/90A battery. The maximum current specification is 9 Amperes. The Package includes ACDN2B, AC6CORD & AC15CORD. ***The AC-DN2B will not charge the BP-M series of Nickel Metal Hydride Batteries***

Cases:

Hard			LC-424CP Grey Case from California Plastics.

LC-424TH Grey case from Thermodyne.

Soft			LC-300SZ											Soft carrying bag with shoulders strap and pockets.

## DXC-D35/D35WS Triax Studio Configuration:

Camera/Triax Studio Packages:

DXCD35TX7DPAC	Includes DXC-D35H Camera, CCU-TX7/1 Triax Camera Control Unit with optional SDI output, RCP-TX7 Remote, CA-TX7 Camera Adapter, DXF-701 SDI output board and DXF-51 B&W Studio Viewfinder.

DXCD35TX7PAC2	Includes DXC-D35H Camera, CCU-TX7/1 Triax Camera Control Unit with optional SDI output, RCP-TX7 Remote, CA-TX7 Camera Adapter, DXF-51 B&W Studio Viewfinder.

DXCD35WTXDPAC

Includes DXC-D35WSL 16:9/4:3 Switchable Camera, CCU-TX7/1 Triax Camera Control Unit with optional SDI output, RCP-TX7 Remote, CA-TX7 Camera Adapter, DXF-701 SDI output board and DXF-51 B&W Studio Viewfinder.

CCU-TX7 Triax only Packages:

CCUTX7DPAC1	Economy component triax package with basic CCU  control, without camera head. Package includes CCU-TX7/1, COU-TX7, CA-TX7 and DXF-701 SDI output board.

CCUTX7DPAC2	Remote control component triax package without the camera head.  It includes full remote controls. Package includes CCU-TX7/1, RCP-TX7, CA-TX7 DXF-701 SDI output board.

CCUTX7PAC1	Economy component triax package with basic CCU  control, without camera head. Package includes CCU-TX7/1, COU-TX7, CA-TX7.

CCU-TX7 Triax only

Packages (cont):

CCUTX7PAC2	Remote control component triax package without the camera head.  It includes full remote controls. Package includes CCU-TX7/1, RCP-TX7, CA-TX7.

## CCU-TX7 Robotic Pan and Tilt Package:

ROBOTICSPAC	This package includes one Fujinon EPT-5E-10DK pan/tilt head and the necessary Interface Module ESI-S01. When connected to a DXC-D35 series camera, it allows the control of one pan/tilt head and one compatible motorized teleconferencing lens through a single cable CCU-TX7 Triax system. The control is accomplished by either the RCP-TX7 remote control panel or by a compatible RS-232 command source (PC) connected to the CCU-TX7. Sixteen complete “Scene File” presets are possible, when used with the RCP-TX7.

## Camera Control Unit  (CCU):

CCUTX7DPAC	The CCU-TX7/1 is a Triax Camera Control Unit with optional SDI Output capability. The CCU-TX7/1 gives the operator complete control of all DSP functions (Skin Tone Detail, Black Stretch and Compress, Dyna-Latitude, etc.) when used with the RCP-TX7 remote control panel. The CCUTX7DPAC package includes the CCU-TX7/1 and the DXBK-701 SDI Output Board.

CCU-TX7/1	The CCU-TX7/1 is a Triax Camera Control Unit with optional SDI Output capability. The CCU-TX7/1 gives the operator complete control of all DSP functions (Skin Tone Detail, Black Stretch and Compress, Dyna-Latitude, etc.) when used with the RCP-TX7 remote control panel. The CCU-TX7/1 can readily accept the new, optional SDI interface board (DXBK-701). A modification kit for older

triax CCU's (model CCU-TX7), is also available. The original features, specifications and functionality of CCU-TX7 and CCU-TX7/1 remains unchanged. The DXBK-701 SDI interface board option must be purchased separately for use with the CCU-TX7/1. Note: The CCU-

TX7MOD/SEL is the model name for the optional SDI

modification kit for the older CCU-TX7.

SDI Output Board:	DXBK-701 SDI Output Board for CCU-TX7/1. It allows two SDI (serial data) outputs. These signals are available at two BNC connectors on the back of CCU-TX7/1. Mounts in open slot inside CCU-TX7/1.

CCU Remote Control:

RCP-TX7 The RCP-TX7 is a control panel that offers full remote camera control for the DXC-D35/D35WS series cameras (The RCP-TX7 can also be used stand alone, and allows complete control the DSR-135/135WS, PVW-D35/D35WS, DSR-500WSL/1, and DSR-300A cameras). It can be connected to the CCU-TX7/1 camera control unit or directly to the DXC-D35 for sophisticated as well as basic control.  It features storage of up to 16 scene files. All parameters for both camera operation and setup can be stored in each scene file. For multi-camera systems, linkage control of Iris and Master black can be set to multiple RCP-TX7 panels. Also, color-matching data for multiple cameras can be copied between RCP-TX7 panels. Control panel includes a LCD panel for menu status information

## and adjustments. The LCD panel also displays troubleshooting hints for RCP-TX7 control.  RCP-TX7 rack size is 1/4 the width of a 19-inch rack, and 4 units can be installed in a standard 19-inch rack with the optional RMM-TXR7//A Rack Mount kit.

##### COU-TX7 The COU-TX7 is a Triax Camera Operating Module provides basic camera control when attached to the front panel of the CCU-TX7 Triax Camera Control Unit. The COU-TX7 is ideal for use in limited space such as mobile field production vehicles. Controls include shutter speed dials, skin detail, gamma settings, auto and manual white/black balance, iris and knee settings. Note: When used with either the DXC-D30WS or the DXC-D35WS camera, the COU-TX7 is unable to remotely switch the camera’s aspect ratio.

CCU-TX7 Triax Rack Mounts:

CCU			RMMTXC7//A

The RMMTXC7//A is the 19" Rack Mount Kit for the CCU-TX7/1. Two CCU-TX7/1 units or one CCU-TX7/1 with a waveform monitor can be mounted in One unit.

RCP	RMMTXR7//A19" Rack Mount Kit for the RCP-TX7 camera remote control panel.  Can mount up to four (4) RCP-TX7 panels.

Camera Adapter:

Triax			CA-TX7

The CA-TX7 is the Triax Camera Adaptor for the DXC-D35/DXC-D35 cameras. It includes two microphone inputs

with return and prompter outputs. It also includes two channel intercom with level contro, and is equipped with a rotary triax connector for easy cabling. Built with rugged

die cast aluminum construction, it has both 76-pin Digital and Pro-50-pin interfaces.  For the DXC-D35, the CA-TX7 is capable of indicating a box cursor in the screen of a viewfinder such as the DXF-51, DXF-41 and DXF-701.

Triax Cable:

½”			CCTA-25 25m (300 ft) 1/2" Triax cable.

CCTA-50 50m (300 ft) 1/2" Triax cable.

CCTA-100 100m (300 ft) 1/2" Triax cable.

CCTA-200 200m (600 ft.) 1/2" Triax cable.

CCTA-300 300m (900 ft.) 1/2" Triax cable.

#### CCTA-400 400m (1200 ft.) 1/2" Triax cable.

CCTA-500 500m (1500 ft.) 1/2" Triax cable.

CCTA-1100 1100m (3300 ft.) 1/2" Triax cable.

3/8”			CCTB-25 25m (75 ft.) 3/8" Triax cable.

CCTB-50 50m (150 ft.) 3/8" Triax cable.

CCTB-100 100m (300 ft) 3/8" Triax cable.

CCTB-200 200m (600 ft.) 3/8" Triax cable.

CCTB-300 300m (900 ft.) 3/8" Triax cable.

#### CCTB-400 400m (1200 ft.) 3/8" Triax cable.

CCTB-500 500m (1500 ft.) 3/8" Triax cable.

CCTB-670 1100m (3300 ft.) 3/8" Triax cable.

RS-232C Cable:	SMF-TX7 RS-232C cable for daisy-chaining Triax control units (CCU-TX7/1). It is 3 ft. long with male 25-pin connectors and allows for master/slave operation of several Triax units.

DXC-D35/D35WS Multicore Studio Configuration:

Camera/Multicore Studio Packages:

DXCD35STPAC1	Includes DXC-D35H Camera, CCU-M5A Multicore Camera Control Unit, CA-537/1 Camera Adapter, DXF-41 B/W Studio Viewfinder, VCT-U14 tripod plate.

DXCD35STPAC2	Includes DXC-D35H Camera Head, CCU-M5A Multicore Camera Control Unit, CA-537/1 Camera Adapter, DXF-51 B&W Studio Viewfinder, VCT-U14 Tripod Adapter.

DXCD35WSSTPAC

Includes DXC-D35WSL 16:9/4:3 Switchable Camera, CCU-M5A Multicore Camera Control Unit, CA-537/1 Camera Adapter, DXF-51 B&W Studio Viewfinder.

## Camera Control Unit (CCU):

CCU-M5A

The new CCU-M5A has been introduced as a replacement/improvement of the very popular CCU-M5. The new CCU has been improved to allow longer cable lengths (300m), audio from the camera and teleprompter

functions when attached to the new CA-537/1 adapter, yet maintaining its very attractive price point and reliability. Note: the 14-pin output connector available on CCU-

## M5 is no longer available on CCU-M5A. If a 14-pin

## connector is required, the Sony Service center can install it at an additional cost.

Camera Adapter:

Component	CA-537/1

The CA-537/1 has been introduced as a replacement of CA-537 and allows a teleprompter output from the Genlock connector. Use with the CCU-M5A and 26-pin Multi-core cable (CCZ-AXX).

Composite or Y/C	CA-327 w/CCU-M5A and 14-pin Multi-core cable (CCQ-	 				XXAM) *Note: CCU-M5A Modification is Required*

CCU Remote Control:

RMM-7G

Miniature remote control for DXC-327, DXC-D30 series, and CCU-M5A. Controls all basic functions.   Optional cables (CCA-7/XX) extend operation to 50 meters.

Studio Viewfinder:

DXF-41 4” B&W Studio Viewfinder (4:3 only)

DXF-51 5” B&W Studio Viewfinder

(4:3/16:9 Switchable)

## Muilticore Cable:

26-Pin			CCZ-A10US 10 meter cable 26-pin male to 26-pin female

(used with CA-537/1)		(33').

CCZ-A25US 25 meter cable 26-pin male to 26-pin female

(82’).

### CCZ-A50US 50 meter cable 26-pin male to 26-pin female

(164’).

CCZ-A100US 100 meter cable 26-pin male to 26-pin

female (333’).

14-Pin			CCQ-10AM 10 meter cable 14-pin male to 14-pin female

(used with CA-327)		(33').

CCQ-25AMUS 25 meter cable 14-pin male to 14-pin					female (82’).

CCZ-50AM/US 50 meter cable 14-pin male to 14-pin

female (164’).

CCZ-100AMUS 100 meter cable 14-pin male to 14-pin

female (333’).

## Cable Accessories

26-Pin Bulk Head

Connector	CCZZ-1B Bulk head connector for CCZ-A cables.

26-Pin In Line

Extension	CCZZ-1E In-line connector for CCZ-A cables.

Notes: