# How to Connect a BRC300 and an Anycast Station via RS-422

## Overview:

The VISCA control protocol uses the RS-232 standard. If a distance of greater than approximately 50 feet (15 meters) is required between a BRC300 and an Anycast Station a VISCA cable cannot be reliably used. The solution is to connect the Anycast’s VISCA port to an adapter that can convert the RS-232 signals to RS-422 signals. The RS-422 signal can be reliably transmitted up to 4000 feet (1.2km).

NOTE: RS-422 does not transmit the RS-232 handshaking signals needed to automatically ID cameras. If “daisy chaining” units together please set each camera’s ID manually via the bottom panel dip switches. Note that RS-422 is bi-directional, “home run” wiring cannot be used.

## Materials:

- Self (not port) powered RS-232 to RS-422 converter (widely available for less than $50)

- 8 pin VISCA to 9 pin D-sub cross cable (Sony Model # RC-815)

- Suitable length of Cat5 cable (or equivalent)

- Phoenix (green) RS-422 Header (supplied with BRC-300)

- Optional 9 to 25 pin adapter may be required depending on converter chosen

## Switch Settings:

- Set the BRC-300 to RS-422 and 9600 baud via the lower panel dip switches.

- Set a unique address for the BRC-300 via the lower panel dip switches.

- If so equipped set the RS-232 to RS-422 converter to “DTE”, “RS422”.

## Wiring:

| VISCA 8 pin | D-sub 9 pin (25 pin) |
| --- | --- |
| Pin | Signal | Signal | Pin |
| 3 | Tx | Rx | 2 (3) |
| 5 | Rx | Tx | 3 (2) |
| 6 | Common | Common | 5 (7) |

| RS-232 to RS-422 Adapter | BRC-300 |
| --- | --- |
| Terminal | Signal | Signal | Phoenix header pin |
| * | Tx + | Rx + | 6 |
| * | Tx - | Rx - | 7 |
| * | Rx + | Tx + | 8 |
| * | Rx - | Tx - | 9 |
| * (optional) | Common | Common | 5 |

(See next page for physical connector layouts.)

## Hook up:

- Connect one end of the Cat5 cable to the RS-232 to RS-422 converter.

- Connect the other end of the Cat5 cable to the Phoenix header supplied with the BRC-300.

- Connect the 9(or 25)-pin end of the VISCA adapter cable to the RS-232 to RS-422 converter.

- Connect the 8-pin end of the VISCA adapter cable the Anycast Station.

- Select the desired ID and operate the camera as normal.