From: Michael

Sent: Wednesday, April 12, 2006 3:23 PM
To: rich@starin.biz
Subject: BRC300 problem

Rich,

We are having an issue with a BRC300 when powered down via a RMBR300.

We get an unstable blue screen instead of a pretty picture.

After going through the power cycle again, most times, the camera will operate normally. So … on every other power cycle from the RMBR300… unstable blue output.

Just 1 camera on the controller, S-vid out.

Any ideas?

Also, is it possible to get a manual for the BRC3000 on-line somewhere?

Thanks for the help.

Michael

Michael,

I’ve never heard of anything like that affecting BRC300 / RMBR300 installations. I’m not sure how you’re are using your cameras or what you are feeding them to, but a little unusual “feature” of the BRC300 cameras might be causing the problem.

For some reason that Sony can’t explain, the BRC300 internal sync generator does not meet RS170A standards for color frame genlock. It just locks H and V and lets the subcarrier assume one of two phases on power up. If you are using genlock and the device you are feeding is sensitive to proper color frame, it might give you this blue screen. Most switchers without frame synchronizers on the inputs will just show you video with the color 180 deg. out of phase, while ones with synchronizers, like the Anycast Station for instance,  will correct the phase error and operate properly.

Every time you reboot the camera, you have a 50/50 chance of it locking in a color frame that matches the genlock signal, so it would appear to be almost every other time you turn it on.

The BRC300 manual is not available at www.sony.com/professional. I might have a pdf of the manual in the office somewhere, but I’m on the road this week and won’t be able to check until next week.

Rich Hoffman

Sony Business Manager

STARIN

Office: (847) 496-4937

Cell: (847) 544-8415