EVID-70 / EVID-100 Control Functions through the RMBR300

Since the EVID70 has no menus which can be selected from the RMBR300 Joystick controller, all you can do is point it. Commands to initiate manual white balance, manual iris and other functions necessary to good operation of the EVID70 must be commanded through the VISCA control protocol.

The functions are controlled by using the PTZ preset buttons labeled 7-16. The list of command functions isn’t published in any manual, but here it is.

| Position | Function |
| --- | --- |
| 7 | AE Auto |
| 8 | AE Brightness |
| 9 | D-Zoom On |
| 10 | D-Zoom Off |
| 11 | WB Auto |
| 12 | WB Manual |
| 13 | WB One Push |
| 14 | WB ATW |
| 15 | ICR On |
| 16 | ICR Off |